## Slide 1: T Level in Design, surveying and planning in construction
Materials to support the contextualisation of science in construction and the built environment

## Slide 2: Framework for Learning
Phases:
building formative scientific knowledge
performing scientific investigations
acquiring data
making informed decisions.
Notes: Provide an overview to explain the sequence of lessons. Advise learners that the outcome of the learning is to be able to select the correct metal materials for industry applications, based on informed knowledge of degradation caused by extrinsic factors.

## Slide 3: 01
Chemical composition of metals

## Slide 4: Atomic composition
An atom has a positive nucleus made of protons and neutrons at its core, surrounded by shells of electrons.
Its structure is comparable to the solar system, in that the orbiting electrons move around a static core.
Electrostatic forces hold the atom together.
Notes: Advise learners that:
The modern view of the atom is called the Bohr model, named after the scientist who first created it (Niels Bohr). It consists of a nucleus that contains protons and neutrons, with smaller electrons orbiting the nucleus.
In this image, the green sphere represents the nucleus, and the red, smaller sphere is the orbiting electron. The letter H indicates that this atom is hydrogen.

## Slide 5: Atomic composition
Notes: Explain to learners:
Everything is made up of atoms.
Elemental atoms consist of only one type of atom; this means they cannot be broken down into multiple substances.
Metals like iron and aluminium are elemental atoms.
When atoms chemically bond together, they make molecules.
Atoms of different elements can combine to make alloys.

## Slide 6: Atomic composition of metals
Watch the video “Atoms explained in simple terms” by MooMooMath and Science and take notes.

## Slide 7: Atomic structure questions
What is the name of the core of the atom?
What are its two component parts?
What is the name of the particles that orbit around the core?
Can you tell me anything else about the atom and its construction?
Notes: Open questions to the group and check their answers.
What is the name of the core of the atom?
A: The nucleus
What are its two component parts?
A: Protons and neutrons
What is the name of the particles that orbit around the core?
A: Electrons
Can you tell me anything else about the atom and its construction?
A: The electrons are considered to be in a “sea”.
A: The number of electrons is different between different atoms.
A: The number of electrons is equal to the number of protons in the core.

## Slide 8: Modelling activity
In allocated groups, construct a model of a named atom.
Refer to the Modelling activity handout for instructions.
Once complete, circulate and review other groups’ models, noting any differences.
Feed back any differences in the models to the rest of the group.

## Slide 9: Atomic composition of metals activity
Working in allocated activity groups:
Use the internet to find an image of a metal bridge, a steel beam and an iron atom.
Discuss how the three images are connected.
Present your connections to the class.
Notes: The connection between atoms, steel beams and bridges lies in the principles of materials science and engineering.
Learners may demonstrate prior learning. Discuss the following and explain that these things will be explored in the next lessons.
1. Atoms:
Everything around us, including steel, is made up of atoms.
Steel is composed primarily of iron atoms, along with small amounts of carbon and other alloying elements.
2. Steel beams:
Steel is a common material used in construction.
In a steel beam, individual atoms are bonded together to form a crystalline structure.
The arrangement of atoms gives steel its mechanical properties.
3. Bridges:
Bridges are structures that span physical obstacles like rivers, valleys or roads, providing a pathway for transportation.
Steel beams are often used in bridge construction because of their strength and ability to support heavy loads.
4. Connections:
The connection between atoms and a steel beam involves the arrangement and bonding of atoms in the steel structure, which determines its properties.
The steel beam, in turn, is a key component in the construction of the bridge: the beams are usually joined together to form the framework or skeleton of the bridge.
5. Engineering principles:
Engineers design bridges to withstand various forces, including tension, compression and shear; the properties of steel, at the atomic level, contribute to its ability to resist these forces.
Welding, bolting and other methods of joining steel beams together create a unified structure that can bear the loads and stresses imposed on the bridge.
In summary, the connection between atoms, steel beams and a bridge is rooted in the atomic structure of steel and how it is engineered and assembled to form a strong and durable structure capable of supporting the intended loads and providing safe passage for transportation.

## Slide 10: 02
Chemical bonding in metals, crystal lattice structures and properties introduction

## Slide 11: Chemical bonding in metals, crystal lattice structures and properties introduction
What you will learn in this session:
process of chemical bonding of metals
creation of crystal lattice structure
introduction to mechanical properties.
Notes: Explain to learners:
The chemical bonding and crystal lattice structure is the underpinning science that informs the properties that the metal will have, and what will happen when deterioration occurs.

## Slide 12: Chemical bonding in metals, crystal lattice structures and properties introduction
Complete the starter activity:
Complete the Parts of an atom starter activity.
You have five minutes to complete this in groups of three.

## Slide 13: Starter activity answer
N _ _ _ _ _ _
E _ _ _ _ _ _ _ _
P _ _ _ _ _ _
N _ _ _ _ _ _ _
U C L E U S
L E C T R O N S
R O T O N S
E U T R O N S
Can you name the atom shown in the diagram?
A _ _ _ _ _ _ _ _
L U M I N I U M

## Slide 14: Chemical bonding in metals
Modelling activity:
Model the molecule allocated to your group, using the colour key.
When instructed, view each other’s models and try to identify the molecules constructed. Note observations about their construction.
You have five minutes to complete this activity.

## Slide 15: Chemical bonding in metals
Atoms colour key for modelling activity
Notes: Note for teacher:
Have this colour key slide on display during the modelling activity if a colour handout is unavailable.

## Slide 16: Representation of molecular structure of aluminium
Photo by Julia Maior on Unsplash
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Al
Notes: Explain to learners:
Think about a piece of aluminum foil and imagine if we had a microscope powerful enough to inspect its molecular structure.
Click three times to progress slide.
It is made up of millions of aluminum atoms, each of which has 13 electrons holding the structure together with its electrostatic force.

## Slide 17: Visual representation of atoms
Solid sphere model of an atom –
John Dalton (1803)
O
Planetary model of an atom with electrons –
Niels Bohr (1913)
O
Nuclear model of an atom –
Ernest Rutherford (1811)
O
Notes: Explain to learners:
All the models shown on this slide are oxygen, which interacts with metals and will be covered in future learning.
These diagrams will be used at different times in the learning, and it is important to understand their relevance and that they represent the same information. The models shown here have evolved at different times and are concurrent with the progression of knowledge about atomic structure.
It is important to become familiar with the presentation of atoms as they are the building blocks of the materials used in construction, specifically metals. To understand the process of deterioration and the properties of the metals connected to this, it is necessary to understand the construction of basics of the metal’s construction.
Although colour is used in the diagrams, atoms do not have a colour and there are no fixed rules about colour allocation. However, it is good practice to be consistent with colour usage.
These diagrams will be used interchangeably in this and future lessons.

## Slide 18: Chemical bonding in metals
Watch the video “GCSE Chemistry - Metallic Bonding #20” by Cognito.
Notes: Notes to teacher:
https://www.youtube.com/watch?v=b1y2Q6YX1bQ
Start the video at 40 seconds and pause at 2:43.
The purpose of this video is to introduce metallic bonding, which will then be expanded upon in the next slides.

## Slide 19: Chemical bonding in metals
Atomic bonding
Atoms can lose or gain electrons.
Atoms are called ions when they lose or gain one or more electrons:
If they lose an electron, they become a positively charged ion (cation).
If they gain an electron, they become a negatively charged ion (anion).
O
ENERGY
Free electron
Nuclear model of an oxygen atom
Notes: Note to teacher:
This is the first in a sequence of three slides to explain chemical bonding.
Explain to learners:
The Rutherford model is used here as it is best able to represent the topic of chemical bonding in metals at this scale.
Atoms are kept together in a regular structure by the electrostatic forces that exist between atoms and electrons. The outer shell of electrons have the weakest forces holding them in place and are easily given up.
However, if energy such as heat is applied, the electrons in the outer shells can become less attached and break free of their original atom and will attach to another, nearby atom.

## Slide 20: Chemical bonding in metals
  Atomic bonding
  As atoms collide, the electrons in the outer shell detach and become free to reattach to another atom.
  This is called metallic bonding.
e-
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
e-
e-
e-
e-
e-
e-
e-
Fe+
Fe+
Fe+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
Notes: Explain to learners:
This image depicts iron atoms (Fe). The atoms are arranged in a regular pattern in a “sea of electrons”. Once free, the atoms become positive ions because they have all lost a negative electron. The free electrons are referred to as delocalised. Although free, there is still a large amount of electrostatic attraction between the positive ions and negative electrons. Because like charges repel and opposite charges attract, as atoms come together to form crystals, cations bond to, and are surrounded by, anions. Anions bond to, and are surrounded by, cations.
This is what holds the pattern of atoms together in a regular structure. It is called metallic bonding.
It is this structure and sharing of electrons that determines the properties of a metal. Manipulation of alloying metals can improve the properties of metals.

## Slide 21: Chemical bonding in metals
Creation of molecules:
The atom is the smallest particle of an element. When two or more atoms chemically bond together, they create a molecule.
Some elements, such as oxygen, have atoms that join in pairs to make the element and can then join other atoms to make new, compound substances.
Fe
Iron atom
Oxygen atom
O
O
O
Fe
O
Iron (II) oxide
(FeO2) atom
Notes: Explain to learners:
Many atoms cannot exist by themselves as they are not stable and must join to other atoms to create chemical stability. For example, iron atoms are always singular and oxygen atoms are always found in pairs — both are elements because they only contain one type of atom, but iron is an element only made up of a single iron atom, while oxygen has two.
When iron and oxygen combine to make iron (II) oxide, there is a single iron atom and a pair of oxygen atoms in each molecule of the new material. This is a compound as there are two elements used to create the molecule.

## Slide 22: Chemical bonding in metals
Pause and reflect:
Discuss answers for the questions in the handout.

## Slide 23: Crystal lattice structure
Watch the video “Metals 101 The Structure of Metals”.
Notes: https://www.youtube.com/watch?v=nXIoOOa7JDI

## Slide 24: Crystal lattice structure of metals
Atomic bonding:
  In the sea of electrons that allow solid structure to exist, the atoms bond and the positively charged metal ions form a 3D crystal lattice structure.
Metals can be distinguished from other materials by their bonding and crystal structures.
The crystal structure also defines their mechanical properties.
Notes: Explain to learners:
Solid metals exhibit a crystalline arrangement, characterised by a unit cell – a specific configuration of atoms that repeats periodically in three dimensions on a geometric lattice.
In this context, atoms can be envisioned as compact spheres within the lattice, forming a consistently repeating and straightforward structure throughout the metal. The arrangement of atoms within this crystalline structure results in varying interatomic spacing, ultimately shaping the metal’s properties. The type of structure created minimises the empty space between the atoms.
The mechanical properties of a metal are significantly influenced by this crystalline structure, as are the outcomes of deterioration actions on a metal. This is important in design and construction to ensure that correct materials are specified in relation to the environments and structural conditions they are expected to endure.

## Slide 25: Crystal lattice structure of metals
Body-centred cubic structure (BCC)
  The BCC structure has one atom at each corner and one at the centre of the cube.
  Metals with a BCC structure include lithium, chromium, vanadium, iron and tungsten.
Face-centred cubic structure (FCC)
  The FCC structure has one atom located at each corner and at the centre of each face.
  Metals with the FCC structure include aluminium, copper, gold, iridium, lead, nickel, platinum and silver.
Hexagonal close-packed (HCP)
  The HCP structure is closely packed. Each layer is offset from the previous, creating great density of atoms.
  Metals that have the HCP structure include beryllium, zinc, magnesium, titanium and zirconium.
(images from www.libretexts.org, 2021)
Notes: Explain to learners:
Metals have one of three basic crystal structure types:​
​
body-centred cubic​ (BCC)
face-centred cubic​ (FCC)
hexagonal close-packed​ (HCP).
The BCC structure has one atom at each corner and at the centre of the cube. Metals with a BCC structure include lithium, chromium, vanadium, iron and tungsten.
​
The FCC structure has one atom located at each corner and at the centre of each face. Metals with the FCC structure include aluminium, copper, gold, iridium, lead, nickel, platinum and silver.​ This structure, along with HCP, has the most efficient packing.
Metals that have the HCP structure include beryllium, zinc, magnesium, titanium and zirconium. In an HCP arrangement of atoms, the unit cell consists of three layers of atoms. The top and bottom layers contain six atoms at the corners of a hexagon and one atom at the centre of each hexagon. The middle layer contains three atoms nestled between the atoms of the top and bottom layers, hence the name “close-packed”. HCP is one of the two simple types of atomic packing with the highest density, the other being FCC.

## Slide 26: Mechanical properties of metals activity
In your groups
Examine the metals:
  Can you squeeze it, bend it or stretch it?
  Does it return to the original shape when you let go?
  Can you make a mark on its surface? Does it scratch easily?
  Is it unusually heavy for its size?

## Slide 27: Mechanical properties of metals research
In your groups:
Research quantitative values for the noted properties of your metals.
Complete the table with this information.
When prompted, share your answers with the class.
Notes: Explain to learners:
Steel is used for bridges because of its strength and ductility. The type of steel may vary according the size and expected loads, but generally it will be high-strength or stainless steel.
Brass is highly malleable and ductile. It can be machined, cast, rolled, hot-stamped and drawn relatively quickly as compared with other metals, making it most suited for making detailed equipment for construction, like screws and fixings.
Copper has a face-centred cubic crystal structure and is a tough, ductile and malleable material. These properties make copper extremely suitable for tube forming, wire drawing, spinning and deep drawing.
Aluminium is the engineering material of choice for many applications. Properties that make aluminium popular and/or suitable include its low density but good strength and ductility at lower temperatures. Aluminium is approximately one-third the weight of steel, copper or brass. Its ductility allows it to be formed and extruded into complex shapes – this, combined with its high strength-to-weight ratio, make it useful for components in windows, doors, roofing, siding and framing.

## Slide 28: Chemical bonding in metals and crystal lattice structure summary
Separate atoms
Atomic bonding creates molecules
Crystal lattices form to create solid structure
Notes: Explain to learners:
Atoms are the smallest part of the structure of any substance.
They bond to form solid matter through the electrostatic forces created between the positive ions and negative electrons.
Atoms of the same type bond to make close-packed structures, and atoms of different types bond to make compound molecules (made of different elements).
Molecules come together in regular pattern structures to form crystal lattices. The type of structure created minimises the empty space between the atoms and determines some of the properties that a metal will have. It also allows understanding of what will happen to a material when it is exposed to adverse weather conditions or certain climatic conditions. It is the science that underpins material deterioration.

## Slide 29: 03
Mechanical properties, behaviour and the tensile test

## Slide 30: Mechanical properties, behaviour and the tensile test
What you will learn in this session:
terminology of mechanical properties
behaviours associated with the terminology
the relationship between a stress-strain graph and the tensile test.

## Slide 31: Identifying molecules starter activity
Complete the starter activity.
Using this key, identify the molecules on the Identifying molecules starter activity.

## Slide 32: Identifying molecules starter activity answers
Answers
Aluminium chloride (AlCl3)
Copper sulphate (CuSO4)
Iron oxide
(FEO2)

## Slide 33: Terminology recap
Strength: The ability of a material to withstand deformation.
Elasticity: The ability of the material to deform and reform from a load applied and removed.
Yield strength: The quantity of load at which the material ceases to respond elastically.
Hardness: The ability of a material to withstand deformation.
?
?
?
?
Notes: Instructions for teacher:
Ask open questions to the class to define the four properties.
Reveal each answer by clicking.
Explain to learners:
This terminology is used to describe key mechanical properties of metals and other materials. It is important to recognise these properties in materials to enable the selection of the correct materials to do a specified job in constructing a building. This is called being “fit for purpose”.
Advise learners of other words that will be used alongside the new terminology and to refer to the glossary.
Force: strength or energy as an attribute of physical action or movement.
Load: the weight or pressure from a force.
Deformation: the act of something changing shape in response to an applied load.
Ask learners to explain the words. Click to reveal answers on the slide.
Strength: the relationship between the external loads applied to a material and the resulting deformation or change in material dimensions.
Elasticity: the ability of the material to deform and reform from a load applied and removed.
Yield strength: the quantity of load at which the material ceases to respond elastically.
Hardness: the ability of the material to withstand surface indentation and scratching.

## Slide 34: Mechanical properties terminology
Elasticity
The ability of a material to deform and reform from a load applied and removed.
Plasticity
  The ability of a material to undergo permanent deformation (non-reversible change in shape) in response to an applied load.
Notes: Advise learners:
These terms are engineering terminology and are used to describe specific properties and associated behaviours. It is important to know if a material will behave plastically or elastically to allow correct decision-making when choosing materials for the design of construction projects. For example, a steel frame for a large warehouse must be strong but have some elastic behaviour to allow it to carry the load of the structure and have some flexibility to resist other forces, such as the wind.
Explain to learners:
Elasticity is the property that describes a material’s ability to deform and change shape when under force from an applied load, but when the load is removed, the material will return to its original shape.
If when the load is removed the material does not change shape, the material has become permanently deformed and any continued change in shape is referred to as plasticity. A material must go through an elastic phase before it either breaks or behaves plastically.

## Slide 35: Mechanical properties terminology
Strength
The ability of a material to withstand deformation.
Yield strength
The quantity of load at which the material ceases to respond elastically.
Stiffness
The ability of a material to resist the application of an external force.
Notes: Advise learners:
This slide highlights key terminology used in material science. They are terms used to describe the expected properties of a material. Strength and yield strength are quantifiable and as such can be used in structural calculations when designing structure. Also, refer to glossary.
Explain to learners:
When a material is deformed, it changes in shape in response to the force applied. Strength refers to the ability of a material to accommodate a force or load without breaking.
It is a total measure of the capacity of the material to withstand the load placed on it before reaching the point of permanent deformation. Engineers often associate strength with a value known as yield strength. The yield strength is measured at the point where the elasticity of the material ends.
Stiffness of material is the ability of a material to resist the application of an external force and is measured by the deflection or change in shape of the material. The smaller the change in shape, the stiffer the material. The greater the change in shape, the more flexible and less stiff the material is. It is referred to as the Young’s modulus of a material and can be calculated from the relationship of the amount of load applied divided by the change in shape of the material when in tension.
So, while both strength and stiffness relate to a material’s ability to resist load, they have quite specific meanings. Structural engineers need to know a material’s stiffness and strength to design safe structures, select appropriate materials, distribute loads effectively, predict structural performance, and optimise design efficiency and cost-effectiveness.

## Slide 36: Terminology of mechanical properties in metals
Watch the video “Tensile Testing” by Instron.

## Slide 37: Introducing the tensile test and the stress-strain graph
F
ΔL
A
B
Notes: Explain to learners:
The terms elasticity and stiffness can be visually represented by a graph.
The graph shows a force being applied to a material on the vertical y axis and the change in shape of the material in response to the force on the horizontal x axis. The change in length is symbolised by “delta” and “L”. Delta means change and L means length (this is sometimes referred to as elongation or extension).
As the force upon the material increases, the shape changes and elongates. Consider that the material is in tension and the forces that apply the load are pulling the material from each end. When the force is removed, the material goes back to its original shape and can be described as having behaved elastically (pull an elastic band to show this effect). The end of each graph line is the end of the elasticity of the two materials and represents the yield strength of each material.
Click for next action.
Here, both materials A and B are behaving elastically. As the force increases, note the change in length.
Click for next action.
When the force is removed, the materials go back to their original shape. Both materials have displayed elastic behaviour.
Click for next action.
Material B, though, has changed length more than material A, and it took less force to make this happen.
This means that material A is both stiffer and stronger because it was better able to resist deformation (less change in shape) and also received more force while resisting. On the graph, the steeper the line that represents elastic behaviour, the stiffer the material is.
Understanding the elastic behaviour of a material and predicting how it will respond to applied forces, including the amount of force and elongation, is crucial in the design of structures for several reasons:
1. Safety: knowing the elastic behaviour helps engineers ensure that structures can withstand expected loads without experiencing excessive deformation or failure. This is essential for ensuring the safety of buildings, bridges and other infrastructure.
2. Efficiency: by accurately predicting how a material will respond to loads, engineers can design structures with the appropriate amount of material. This ensures that structures are both safe and cost-effective, as they use only the necessary quantity of materials without excess.
3. Durability: understanding elastic behaviour helps in designing structures to withstand repeated loading and unloading cycles without suffering from fatigue or permanent deformation. This is crucial for ensuring the long-term durability and reliability of structures.
4. Functionality: designing structures with the correct amount of elasticity allows them to perform their intended functions effectively. For example, buildings should be able to withstand wind and seismic forces without excessive movement, while bridges should be able to expand and contract with temperature changes without causing damage.
Knowledge of elastic behaviour and the relationship between force and elongation is essential for designing safe, efficient, durable and functional structures that can withstand expected loads and environmental conditions.

## Slide 38: Introducing the tensile test and the stress-strain graph
B
STRESS = F/ CSA
σ
STRAIN = ΔL/Lo
Notes: Explain to learners:
The test that is performed is called a tensile test, and the graph that is generated from the test is called a tensile graph or a stress-strain curve. Tensile testing is performed on materials to evaluate their mechanical properties, specifically their response to tensile (pulling) forces.
Some properties of materials can be observed in a stress-strain curve. Knowledge of the stress-strain curve allows engineers to compare different materials and predict the behaviour of a part or full structure made from a particular material (e.g. stiffness and failure strength).
Tensile testing is a way to see how materials behave when they are pulled apart. Force and change in length are the two quantities that are measured during tensile testing. The force is how load is pulling the material, and the change in length is how much it changes shape.
Engineering stress and engineering strain are the words used to describe what is happening to the material during testing.
Engineering stress is how much force is being applied per cross-sectional area.
Engineering strain is asking: how much does the material change in length compared with its original length?
These terms help to compare materials of different sizes and understand how much the material is stretching or deforming. Note the symbol used to represent stress, σ. This is called sigma, and the symbol for strain, ϵ, is called epsilon.
So, by converting force and change in length to engineering stress and engineering strain, the raw data measurements are put into a form that’s easier to understand and make comparisons between different materials and sizes. There is a formula to help convert the raw data.
This is done by dividing the load applied to the material (the force) by the initial cross-sectional area of the sample in the test and dividing the amount it changes in length by the original length of the material (Lo).
Understanding the engineering stress and engineering strain of a material is invaluable in construction and design for several reasons:
1. Material selection: it provides crucial information about how a material will behave under load, helping engineers select the most appropriate materials for specific construction applications. For example, in building structures, materials with higher engineering stress and strain values may be preferred, to ensure structures can withstand anticipated loads without failing.
2. Structural design: knowing the engineering stress and engineering strain of materials allows engineers to design structures that can safely accommodate expected loads and deformations. This ensures that buildings, bridges and other structures are structurally sound and meet safety standards and regulatory requirements.
3. Performance prediction: engineering stress and engineering strain data enable engineers to predict how materials will perform over time under various environmental conditions, such as temperature changes, moisture exposure and seismic activity. This information is essential for assessing the long-term durability and performance of constructed assets.
4. Optimisation: by understanding the characteristics of materials, engineers can optimise the design of structures to minimise material usage while ensuring adequate safety margins. This can lead to cost savings and more efficient construction practices.
5. Failure analysis: in the event of structural failures or performance issues, knowledge of engineering stress and engineering strain can help engineers analyse the root causes and implement corrective measures to prevent future failures.

## Slide 39: Calculating Young’s modulus
k = STRESS / STRAIN = Stiffness = Young’s modulus
B
STRESS
σ
STRAIN ϵ
k
Notes: Explain to learners:
The graph is now showing the material’s response to applied force and change in length.
Stiffness is measured using a value called Young’s modulus and can be calculated from the stress-strain graph. This is a numerical constant that exists during the elastic region of deformation in a material. This is a specific form of Hooke’s law of elasticity. The units of Young’s modulus in the metric system is Newtons per square metre (N/m2).
Click for next action.
Young’s modulus can be calculated by dividing a y value for any point of the elastic graph by the corresponding x value.
Young’s modulus is meaningful only in the range in which the stress is proportional to the strain, that is during the elastic region of the graph, and the material can return to its original dimensions when the external force is removed.
Click for next action.
k represents the gradient of the graph line and is also calculated by taking a point on the graph and dividing the y value by the x value that corresponds to that point.
So, the stiffness of a material is represented by its ability to resist the application of external force, and the steeper the graph line, the greater that resistance is. The gradient of the graph line is equal to the material’s stiffness and Young’s modulus.
Where k is used to represent gradient, a capital E is used to represent Young’s modulus.

## Slide 40: The behaviour of the metal sample
STRESS
STRAIN
ELASTIC LIMIT
FRACTURE
YIELD POINT
PROPORTIONAL LIMIT
ULTIMATE TENSILE STRENGTH
ELASTIC REGION
PLASTIC REGION
Notes: Explain to learners:
Once the elastic behaviour ends, the material will either break or continue to extend and deform but not return to the original shape. This point is called the proportional limit. It is the point in the deformation of the material where the strain is no longer proportional to the stress. After this point, it is no longer possible to calculate Young’s modulus from the steepness of the graph.
Click for next action.
The formation of the arc represents the continued deformation of the metal while in tension. Although the material may experience some return to its original shape if the force is removed, it will not return fully to this shape.
Click for next action.
The specific point where all elastic behaviour ends is called the elastic limit. After this point, the metal briefly undergoes an elastic-to-plastic transition known as elastoplasticity. All the behaviour before this point is in the elastic region. Once this begins, the material has entered the plastic stage of deformation and is behaving plastically.
Click for next action.
All behaviour in the metal after this point is plastic as there is no true elastic response when the force is removed. During this plastic phase, the material cannot return to its original shape and will remain deformed when the load is removed. The tensile graph will rise less steeply and begin to flatten, eventually forming an arc.
When the deformation of the material reaches 0.2% of the original length, the metal is at the yield point.
Click for next action.
At the yield point, the material undergoes permanent deformation without any significant increase in stress. Identifying the yield point is important as it helps engineers understand a material’s behaviour under stress and determine a material’s practical limits in structural applications.
The yield point also represents a critical stage in the change of molecular structure of the material. Before the yield point, the atoms are arranged in the lattice structure typical of the type of material. Before the yield point, during the elastic region, the bonds between atoms and molecules start to stretch, leading to elastic deformation – but without stretching beyond their limit, meaning that when stress is removed, they reform. At the yield point, the stress applied becomes sufficient to cause some of the bonds between atoms to permanently deform or break. This leads to the initiation of dislocations within the material’s crystalline structure. Dislocations are defects or irregularities in the lattice arrangement of atoms.
As the material continues to elongate, the dislocations extend through the material and the material undergoes significant deformation, leading to a permanent change in shape. The movement of dislocations represents the onset of plastic flow within the material, which continues until the material ultimately fails or fractures under further stress.
Click for next action.
When the graph ends, the material has failed. This is the point of fracture.
Click for next action.
The plastic phase can be further split into two distinct parts –the uniform plastic deformation and non-uniform plastic deformation. The first stage of plastic deformation is from the elastic limit to the ultimate tensile strength. The ultimate tensile strength represents the strongest the material can be while under tensile force. In this first stage, the breaking of atomic structure and creation of dislocations is happening through the entire structure of the material – hence, uniform plastic deformation. However, after the ultimate tensile strength, the weakest of these dislocations, which is usually in the middle, becomes the focal point for the deformation and all the energy that is absorbed to eventually fracture the material is focused here – hence, non-uniform plastic deformation.

## Slide 41: Properties observed in the tensile test
Hardness
The ability of a material to withstand surface indentation and scratching.
Notes: Explain to learners:
There are two more terms that relate to mechanical properties – hardness and toughness. These are directly related to the molecular structure of the material and not as easy to see from a graph representing the material behaviour.
Hardness is a metal’s ability to withstand surface indentation (localised plastic deformation) and scratching. Because the tensile test does not affect the surface of the metal, hardness cannot be measured from the test. However, typically brittle metals usually demonstrate a high level of hardness, whereas a ductile material does not.

## Slide 42: Properties observed in the tensile test
Toughness
  The ability of a material to absorb energy and plastically deform without fracturing.
Brittle Material
Ductile Material
Notes: Explain to learners:
Comparable toughness can be observed from graphs but not directly measured from the graph. It is visually represented by the area underneath the curve in the graph. The bigger the area, the more energy was needed to deform and fracture the metal and the tougher the material is.
This means that two materials can be tested and from their graphs it can be observed which of the two is tougher, but not directly quantified.
The graphs depicted here show a brittle material with less toughness than a ductile material.

## Slide 43: Properties observed in the tensile test
Hardness
The ability of a material to withstand surface indentation and scratching.
Toughness
  The ability of a material to absorb energy and plastically deform without fracturing.
Notes: Explain to learners:
There are two more terms that relate to mechanical properties – hardness and toughness. These are directly related to the molecular structure of the material and not as easy to see from a graph representing the material behaviour.
Comparable toughness can be observed from graphs but not directly measured. It is demonstrated by the area underneath the curve in the graph. The bigger the area, the more energy was needed to deform and fracture it. This means that two materials can be tested and from their graphs it can be observed which of the two is tougher.

## Slide 44: Terminology of mechanical properties in metals
Watch the video “Material Properties 101” video by Real Engineering.

## Slide 45: Relationship of chemical bonding in metals to properties
Body-centred cubic structure
Face-centred cubic structure
Hexagonal close-packed
(www.libretexts.org, 2021)
Notes: Explain to learners:
Some of the properties of metals are directly related to the crystal structure of the material – the way atoms, ions or molecules are spatially arranged.
The three main formations of metallic crystal lattice are body-centred cubic structure (BCC), face-centred cubic structure (FCC) and hexagonal close-packed (HCP). Each support different mechanical properties and their associated behaviours.
In the BCC, the packing of the crystal formation is smaller than other crystal structures and produces a metal with, usually, increased hardness and strength and low ductility. This is typified by metals with this formation such as iron and tungsten.
Ductile-to-brittle transformation, which occurs when the metal are exposed to varying temperatures, is common to metals with this structure. This occurs when heating or cooling the metal and changes the atomic form in the lattice, moving it from BCC to FCC. Iron has a BCC structure, but when heated above 912°C, it transforms into an FCC structure. This means materials can be manipulated to improve certain properties. For example, when iron is heated, it can be blended with carbon to become steel, which is harder. When it cools again, the carbon and iron alloy has become much harder than in the pure iron form. This is the basic chemistry of the creation of carbon steel or high-strength steel.
In the basic FCC structure, there are 14 atoms. Metals with this formation include copper, aluminium and platinum. FCC metals are very ductile.
Finally, HCP structures are often semi-ductile. This means that they are not as ductile as an FCC metal but not brittle like a BCC metal. Examples of metals with a HCP structure include magnesium, titanium and zinc.

## Slide 46: Relationship of chemical bonding in metals to behaviour
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Fe+
Notes: When a force is applied, the molecules are pushed within their lattice structure.
Imagine that lattice structure is a series of identical-shaped spheres, and they can be pushed over their adjacent molecular spherical layers.
Click for next action.
If the layer being pushed does not go further than the highest point of the layer below, it can return to its original position when the force is removed. This is elastic behaviour – i.e. the deformation is not permanent. The bonds holding the molecules together have been stretched but not broken and, as such, when the force is removed, the elasticity will pull them back to the original shape.
Click for next action.
If the layer of spheres are pushed over the layer below, then they cannot return and have behaved plastically – i.e. deformation is permanent. Here, the bonds were broken to cause the deformation, but because new bonds will form, a new formation of molecules exists; remember that the delocalised electrons making the bonds must reattach after they detach, which keeps the structure solid.
This explains ductility as well. The sea of delocalised electrons will adjust to the new formation to keep the metal intact, but the metal may have a new, “deformed” shape compared with its original one.

## Slide 47: Properties of metals summary
A
B
C
D
Notes: Explain to learners:
Material A is brittle; it shows no plastic deformation when force is applied in tension, only elastic. Because the gradient of the line is so steep, and there is very little elongation of the material for a large amount of force applied, the material is very stiff. The ability of the material to resist the increasing load suggests that it is strong. All these properties indicate that the material will probably have a BCC structure and would also be very hard.
What kind of metal do you think A might be?
A: Iron or tungsten
Material B is also brittle, but not as strong as A because it failed before the same amount of force was applied. However, it is still strong compared with C and D. The material appears to be entering the plastic phase but fails quickly, demonstrating an apparent yield strength but no ductility. This might be high carbon steel wires. The carbon gives them strength. This may be an HCP material.
Material C is ductile – it has an elastic phase and then a large plastic phase. Because of this, it is not brittle. The amount of space under the graph indicates that that a large amount of energy was used to deform and finally fracture the material, and so it is also tough. This material probably has an FCC structure because it is very ductile.
What kind of metal do you think C might be?
A: Aluminium alloy or copper.
Material D has very little elastic behaviour but lots of plastic deformation. This material is called a plastic material because of this and is unlikely to be a metal.
Explain to learners:
As well as the individual properties being determined from the graph shape, it is possible to compare materials’ properties. This means that when designing for a construction project and making choices about the materials, the most mechanically suitable material can be selected:
The material that reaches the highest up the y axis is the strongest.
The material with the furthest elastic limit across the x axis is the most elastic.
The material that stretches the furthest across the x axis, completely to point of fracture, is the most ductile.
The material with the steepest elastic region is the stiffest.
The material with the largest amount of area under the graph is the toughest.

## Slide 48: 04
The tensile test

## Slide 49: The tensile test
What you will learn in this session:
how to conduct a tensile test
what happens to the test sample during the tensile test
how to interpret the stress-strain graph.

## Slide 50: The tensile test
All materials have potential mechanical energy.
Notes: Explain to learners:
Potential mechanical energy is the energy transferred to an object by work when an external force displaces or deforms the object.
It is a scalar quantity, i.e. it has only magnitude or a measurable size.
All materials have potential mechanical energy, which can be observed when the tensile test is conducted.
Tensile testing provides details of the tensile mechanical properties of a material as defined previously. These properties can be plotted on a graph as a stress-strain curve to show details such as the point at which the material failed, as well as providing details of properties such as the modulus of elasticity, strain and yield strength.
It is conducted in a uniaxial format (one direction) and involves stretching a material and noting the force in relation to extension of the material.
The graph that is created is a stress-strain graph.
Tensile testing has a variety of uses in design, surveying and planning, including:
selecting materials for an application
predicting how a material will perform under different forces
determining whether the requirements of a specification, contract or standard are met
providing standard quality assurance data for scientific and engineering functions
comparing technical data for different material options.

## Slide 51: The tensile test
Watch the video “Tensile Testing Basics” by MTS Systems (3 minutes 16 seconds).

## Slide 52: What happens during the tensile test?
STRESS
STRAIN
ELASTIC LIMIT
FRACTURE
YIELD POINT
PROPORTIONAL LIMIT
ULTIMATE TENSILE STRENGTH
ELASTIC DEFORMATION
PLASTIC DEFORMATION
Notes: Explain to learners:
During a tensile test, a metal sample is subjected to gradually increasing tensile (pulling) forces until it fails. Here’s what happens during each stage:
Elastic deformation: initially, when the force is applied, the metal deforms elastically. This means it changes shape temporarily but returns to its original shape once the force is removed. This elastic deformation is characterised by Hooke’s law, which states that the stress is directly proportional to the strain within the elastic limit of the material.
Yield point: as the force increases, a brittle material will fail at this point as the crystalline structure does not have the resilience to stretch the molecular bonds.
A ductile metal starts to undergo plastic deformation, meaning it deforms permanently even after the force is removed. The yield point marks the transition between elastic and plastic deformation.
Plastic deformation: beyond the yield point, the metal continues to deform plastically. The stress-strain curve becomes nonlinear, and the material undergoes significant deformation without fracturing. The metal grains begin to slip past each other, causing the material to elongate.
Fracture: eventually, the metal sample fractures, usually at its weakest point, which is often within the necked region. This marks the ultimate tensile strength (UTS) of the material, which is the maximum stress it can withstand before breaking.
By analysing the stress-strain curve generated during the test, engineers can determine various mechanical properties of the metal, such as its elastic modulus, yield strength, ultimate tensile strength and ductility. This allows structural engineers to understand how a material will perform when being specified for a building or structure.

## Slide 53: What happens during the tensile test?
Molecule
Atom
Covalent bond
Notes: Explain to learners:
Different materials behave differently according to their density and crystalline structure, among other things, and this is reflected in the type of graph that we see when we test them.
A brittle material will often display greater strength as there is very little engineering strain (linear deformation on the x axis) in response to the engineering stress (force being applied, shown on the y axis). It will display almost all elastic deformation and no plastic behaviour as the material absorbs less energy during the process.
Click for next action.
Molecular structure of a brittle material is often exemplified by covalent bonding, where two or more atoms share electrons. This sharing of electrons in the outer shell creates a very strong bond, not reliant upon the electrostatic forces, and it would require more energy to remove the electrons than would be gained by making new bonds. Each atom gives one of its outer electrons to the electron pair, which then spends some time with each atom. Consequently, both atoms are held near each other since both atoms have a share in the electrons.
In each molecule, the bonds between the atoms are strong but the bonds between molecules are usually weak. This makes many solid materials with covalent bonds brittle.
When force is applied, the material displays minimal elasticity (stretching of the atomic connections) as it is not absorbing energy but displays sudden fracture as the molecular bonds reach their limit.

## Slide 54: What happens during the tensile test?
Brittle materials
Valence electrons
Molecule
Atom
Notes: Explain to learners:
Ductile materials are most often metallic and have between one and three electrons in the outer shell. The bond between these electrons and the nucleus is weak and they often break free of the shell, becoming “free electrons”. These valence electrons have mobility between the atoms, making the bonds between atom and electron delocalised. This sharing of electrons creates regular crystalline structure in the material and makes it possible for the atoms to slide past each other when the metal is being deformed under stress, instead of fracturing like a brittle material.
Click for next action.
This takes more energy and more absorption of energy and generates plastic behaviour. The atomic structure is weak because of its ability to be stretched and for the electrons to reattach, but the molecular strength is also greater because of this.
The fracture of the material comes after elastic extension has taken place and the material deforms plastically, eventually fracturing in response to the stress applied as the bonds are stretched and pulled apart.

## Slide 55: What happens during the tensile test?
Ductile materials stress strain curve:
Strain
Stress
Proportional limit
Yield point
Ultimate
tensile strength
Fracture point
Strain hardening Necking
Notes: Explain to learners:
During the tensile test, the metal’s shape changes as the load is applied and increased.
One of the stages in the stress-strain curve during the plastic deformation is the strain hardening region. This region starts as the strain goes beyond the yield point, and ends at the ultimate strength point, which is the maximal stress shown in the stress-strain curve. In this region, the stress mainly increases as the material elongates, except that there is a nearly flat region at the beginning. Strain hardening is also called work-hardening or cold-working, because the plastic deformation occurs at a temperature low enough that atoms cannot rearrange themselves.
This rearrangement occurs because of dislocations in the metal. Dislocations are irregularities in the structure of a metal and arise from misplacement of bonds of the atoms in a part of the plane of a crystal. They are instrumental in affecting the breaking stress and plastic and chemical properties of crystals. The importance of dislocations lies primarily in the fact that they can move.
When a metal is plastically deformed, any dislocations in the structure move, and additional dislocations are generated. Dislocations can move if the atoms from one of the surrounding planes break their bonds and re-bond with the atoms at the terminating edge. The dislocation density in a metal increases with deformation or cold work because of dislocation multiplication or the formation of new dislocations. The more dislocations within a material, the more they will interact and become pinned or tangled. This will result in a decrease in the mobility of the dislocations and a strengthening of the material. This is apparent on the graph as the material appears to be becoming stronger, rising higher up the y axis of the stress-strain graph.

## Slide 56: The tensile test
Watch the video “An Introduction to Stress and Strain” by The Efficient Engineer (to 6:10 only).

## Slide 57: Stress-strain graph interpretation
Using the Tensile testing instructions handout, complete tasks one and two.

## Slide 58: The tensile test
Complete tensile test.
Notes: Guidance for teacher:
If you are unable to complete tensile testing, there is data available in the form of Excel spreadsheets.

## Slide 59: Stress-strain graph creation
Create the stress-strain graph.
Use the data from the test to plot the stress-strain graphs for your chosen metals.
Use the How to plot graphs in Excel instructions.

## Slide 60: The tensile test interpretation
Watch the video “Using a Stress Strain Graph to Compare Properties of Materials” by Jumeirah College Science.

## Slide 61: 05
Force and load

## Slide 62: Force and load
What you will learn in this session:
basic units used to describe force and load
load on simply supported beams – types, point, uniformly distributed load
forces – tension, compression, shear and bending
equilibrium, bending moments and shear force.

## Slide 63: Force and load basic units
What is mass?
The mass of an object is a fundamental property of the object. It is a measure of the amount of matter in the object.
The symbol for mass is m.
Its SI unit is the kilogram (kg).

## Slide 64: Force and load basic units
What is force?
  A force is an influence or action on a body or object that causes – or attempts to cause – movement.
  The symbol for force is F.
  The SI unit for force is kg.m/s2 or N (Newtons).

## Slide 65: Force and load basic units
Why is it called a Newton?
Newton’s second law of motion (paraphrased):
“The net force applied to a mass is equal to the mass multiplied by the acceleration.”
The symbol for acceleration is a.
The SI unit for acceleration is m/s2.

## Slide 66: Force and load basic units
What is the relationship between mass and force?
When force is applied to a mass, acceleration (movement) is produced.
The greater the mass, the more force is needed to accelerate the object.

## Slide 67: Force and load basic units
What does this mean?
  This implies that force is associated with how fast we can make something move. This can be expressed as an equation:
  Force = mass x acceleration (F = m.a)

## Slide 68: Force and load basic units
Gravity is a force:
All things that have mass, have gravity. It is a mutual attraction or “pull” between objects with mass.
The bigger the object, the greater its mass.
The symbol for gravity is g.

## Slide 69: Force and load basic units
What is weight?
Weight is the mass of an object multiplied by acceleration caused by gravity.
The symbol for weight is W.
The SI unit for weight is N (Newton).

## Slide 70: Force and load basic units
What is weight?
Weight can be expressed as an equation:
Weight = mass x acceleration (caused by gravity)
  W = m.g

## Slide 71: Force and load basic units
  Weight = mass x acceleration (caused by gravity)
  W = m.g
This is the same as: Force = mass x acceleration
  F = m.a
So, this implies there is a relationship between weight and force.

## Slide 72: Force and load basic units
On earth, acceleration caused by gravity is 9.8m/s².
For every second an object is in free fall, its speed increases by 9.8 metres per second.
If rounded up to 10m/s², then:
1kg (mass) = 10N (Newtons)

## Slide 73: Force and load basic units
W = m.g
1N = m x 10m/s2
m = 1N x 10m/s2  m = 10N/m/s2

## Slide 74: Force and load basic units
The degree of compactness of a substance is the density.
The mass per unit of volume (kg/m³).
  Density = mass / volume
  The usual symbol for density is  (rho) or D
  and its SI unit is kg.m3

## Slide 75: Force and load basic units terminology quiz
Complete the Force and load basic units terminology quiz.

## Slide 76: Load types
In design, surveying and planning, load is often referred to.
It is the force that is being applied to the structure.
There are different types of load that apply force upon a structure.

## Slide 77: Load types
  Dead load
  This is the permanent load acting upon a structure, including the self-weight of structural elements, such as concrete frames, and any non-structural elements that form a permanent part of it, such as the roof.
  It is sometimes called static load.
Photo by Simone Hutsch on Unsplash.
Notes: Explain to learners:
Calculating dead loads accurately helps in designing foundations, columns, beams and other structural components to meet safety standards and prevent structural failures.

## Slide 78: Load types
  Live load
  This is the weight of everything superimposed upon the structure, such as people, furniture, equipment, machinery, etc. – anything that can be taken away from the structure. It includes weight that changes over time and transient forces. It is sometimes called imposed load.
  It can include certain transient weather phenomenon, such as snow.
Photo by Julia Joppien on Unsplash.
Notes: Explain to learners:
Imposed loads play a crucial role in the design of buildings.
Safety verification: when designing a building, engineers need to ensure that the structure can safely support all the loads it will experience during its lifetime. Imposed loads, which arise from occupancy and usage, are an essential part of this verification process. Without considering these loads, we cannot accurately assess the structural safety.
Occupancy and usage: imposed loads include factors such as normal use by people, furniture, movable objects and vehicles. For example, the weight of people walking, furniture and equipment all contribute to the overall load on the structure. By calculating these loads, we ensure that the building can withstand the forces it will encounter.
Design efficiency: properly accounting for imposed loads ensures that structural elements are dimensioned efficiently. Over-design leads to unnecessary costs, while under-design compromises safety. By considering the actual loads, engineers strike a balance between safety and economy.
Imposed loads are essential for designing safe and efficient buildings. They help engineers verify the structural integrity and ensure that the building can withstand real-world usage.

## Slide 79: Load types
  Seismic load
  These are forces that a structure experiences when earthquake activity occurs. The loading is horizontal and interferes with the structure’s inertia.
Photo by Library of Congress on Unsplash.
Notes: Explain to learners:
Seismic load refers to the force exerted on a structure during an earthquake. It is a horizontal force that shakes the building.
Buildings are inert – this means that they stay still and tend to not move. During an earthquake, the mass of the building resists the horizontal movement, and this is sometimes referred to as inertial load.
Seismic load is an important consideration in the design of structures in earthquake-prone regions, as it can cause significant damage or failure if not properly accounted for.

## Slide 80: Watch the video
Watch the video “Why do Buildings Fall in Earthquakes?” by Vicki V. May (TED-Ed).

## Slide 81: Load application
Load is generally transferred by two methods:
point loading
uniform distributed loading.

## Slide 82: Load application
Point load
Notes: Explain to learners:
Click for next action.
Point load is an application of force at a concentrated area of the structure of a building, such as a person standing on the floor.
Click for next action.
Or the placement of a wall perpendicular to a beam upon which it sits.

## Slide 83: Load application
Uniform distributed load
Notes: Explain to learners:
Click for next action.
A uniform distributed load (UDL) is load that is distributed evenly over an area or length of a structural element. A UDL has the same value at any point along the structural element, such as a beam. A UDL can be any of the types of loads, but an example would be snow on a roof, or a wall constructed along the length of a beam.
Its force is measured in kN per metre. As with all loads, it is critical to understand the loading to design safe buildings than can withstand force.

## Slide 84: Load transfer
Notes: Explain to learners:
In a typical house structure, load transfer refers to the process by which the weight of the building and its contents are distributed and supported by various structural elements, ultimately transferring the loads to the foundation and the ground. Below is a simplified explanation of load transfer in a typical house structure:
It starts with snow.
Click for next action.
As it snows, the snow settles on the roof of a building.
The weight of the snow transfers its load across the whole area that it covers and, along with the roofing materials such as tiles, is initially transferred to the roof trusses or rafters. These structural elements are designed to distribute the load evenly across to the exterior walls of the house.
The load from the roof is transferred vertically downwards to the exterior walls. The walls act as load-bearing elements, supporting both vertical and lateral loads within the structure. The weight of the walls themselves, as well as any additional loads such as wind or seismic forces, is transferred to the foundations.
The weight of the floors, including the floor joists and any additional loads such as furniture and occupants, is transferred to the interior load-bearing walls and ultimately to the foundation.
Inside the house, more load-bearing walls help distribute the weight of upper floors and roof loads to the external walls or foundation. These walls are strategically placed to support the vertical loads and prevent excessive deflection or deformation of the structure.
The foundation of the house serves as the base upon which the entire structure rests. It is designed to transfer the loads from the walls, roof and floors to the ground beneath. The foundation can be made of materials such as concrete or reinforced masonry, providing stability and support for the entire structure.
Click for next action.
Overall, load transfer in a typical house structure involves a coordinated system of structural elements working together to support and distribute the weight of the building and its contents, ensuring stability and safety for occupants.

## Slide 85: Pause and reflect
When prompted, provide an example of something in the room or building that you are in:
  state the type of load
  state how it applies force to the structure
  explain the load transfer.
Notes: Explain to learners:
As an example, a table is a live load, and it applies force through point loading (from the legs) onto the floor. This passes through the floor to the wall and down to the foundations. At each point of connection between the elements of structure, there is either a point load or UDL transferring the load.

## Slide 86: Equilibrium
  If an object is stationary, as a building or any part of it normally is, it is in a state of equilibrium.
  This means that any force on it must be opposed by another force, equal in magnitude but opposite in direction.
  This is Newton’s third law of motion.
Notes: Explain to learners:
Newton’s third law of motion tell us that there needs to be equal and opposite forces actioning upon a static body for it to be in equilibrium and that if an object such as a building is stationary, then any force upon it must be being opposed by a force of equal magnitude in the opposite direction.

## Slide 87: Equilibrium
Equilibrium is the state of an object where all the forces acting on the structure are in balance and no movement occurs.
The sum of forces (including support reactions) must be zero in both horizontal and vertical directions.
The sum of moments (torques) about any axis must also be zero.
Notes: Explain to learners:
That reactions are the equal and opposite forces that maintain the equilibrium with the applied forces.
A moment refers to the internal forces of a structural element that lead bending and deformation (change of shape) when under force. Understanding moments helps optimise material usage and prevent failure. Moments are analysed to ensure structural integrity when designing structures.

## Slide 88: Compression and tension and internal force reactions
Compression
Tension
Notes: Explain to learners:
When an external load is applied, the atomic structure inside a metal element is pushed and pulled and to maintain equilibrium. The reaction from the internal structure must be equal to that of the external applied load, although there may be some deformation from the structure if the external loads are greater.
When an external load pushes down on the structure the structure pushes back, this causes compression. When the external loads are pulling away, the internal forces pull the opposite way, causing tension.
The forces of compression and tension can be represented by the arrows at the top and bottom of the column.
These forces must be opposed by opposite and equal forces pushing up and down to maintain equilibrium.

## Slide 89: Compression and tension and internal force reactions
Education & Training Foundation
Notes: Explain to learners:
Click for next action.
When a point load is applied to a beam, it experiences internal forces in response to the external loads, as explained on the previous slide.
The point load creates a downward force on the beam. This cause deflection (bending in response to the external load).
Click for next action.
Imagine that the beam has nails sticking out of it, top and bottom. The nails represent the molecules of the material the beam is made from.
Click for next action.
As the force is applied from the top, the top side of the beam experiences compression as it gets squeezed together. The nail heads will come closer together to represent this.
As the bottom side of the beam experiences tension, the nail heads on the underside move further apart. The greater the force from above becomes, the further apart the nail heads will move.
The molecules on the top side of the beam are squashed or in compression.
The molecules on the bottom side of the beam are stretched or in tension.

## Slide 90: Compression and tension and internal force reactions
Education & Training Foundation
Maximum compression
Maximum tension
Neutral axis
Force
Notes: Explain to learners:
As demonstrated on the previous slide, when loads are applied to a beam, compression and tension occurs on the upper and lower surfaces of the beam. As well as the surface molecules responding to the force, internal forces develop within the beam.
The internal forces generated from the compression and stretching of the molecules increase towards the outside of the beam, in either compression or tension according to which side the force is applied.
Understanding shear forces helps prevent catastrophic failures, especially in bridges, buildings and other large structures.

## Slide 91: Compression and tension and internal force reactions
Normal forces
Shear forces
Compression
Tension
Notes: Explain to learners:
Visualise these internal forces by making an imaginary cut through a beam and consider the internal forces acting on the cross-section. These internal forces have two components:
1. normal forces, which are oriented along the axis of the beam, perpendicular to the beam cross-section
Click for next action.
The normal stresses will be tensile on one side of the cross-section, and compressive on the other. If the beam is sagging, the top of the beam will get shorter, and so the normal forces acting at the top will be compressive. The bottom of the beam will get longer, and so the normal forces acting at the bottom of the beam will be tensile.
2. shear forces, which are oriented in the vertical direction, parallel to the beam cross-section
The internal forces develop in a way that maintains equilibrium. If a section is made through the beam, the internal forces will always balance the external ones.
These forces cancel each other out, so they don’t produce a net force perpendicular to the beam cross-section, but they do produce a moment.

## Slide 92: Compression and tension and internal force reactions
Shear force
Bending moment
Notes: Explain to learners:
This means that the internal forces acting on the cross-section of the beam can be represented by one resultant force, called a shear force, which is the resultant of the internal shear forces, and by one resultant moment, called a bending moment, which is the resultant of the internal normal forces. The resultant is something produced because of something else – in the case of force and load, it is the effect caused by two or more other forces.
Shear force and bending moment calculations are used to design beams. Understanding how the shear force and bending moments can be different at different locations on the beam allows designers to quantify the size and volume of a beam suitable for the expected loads.

## Slide 93: Load, compression and tension in bridges
The basic bridge is a simple beam structure between two supports.
The principles of internal forces can be demonstrated by imagining someone walking across the bridge.
Photo by Zach Searcy on Unsplash.
tension
compression
Notes: Note to teacher:
Image depicts basic bridge formation.

## Slide 94: Load, compression and tension in bridges
By adding more supporting elements, a basic bridge could span a greater distance.
Photo by Silas Baisch on Unsplash
tension
compression
Notes: Explain to learners:
In a deck bridge, compression and tension forces play crucial roles in supporting the weight of the bridge deck and transferring loads to the supporting elements.
In a deck bridge, compression forces primarily act on the vertical members (such as the piers or columns) that support the bridge deck. These vertical members are subjected to the downward force exerted by the weight of the bridge deck, vehicles and any other loads. The piers or columns of the deck bridge experience compression forces as they support the weight of the bridge deck and transfer the loads to the foundation or substructure below.
The tension forces primarily act on the horizontal members (such as the beams or girders) that support the bridge deck. These horizontal members are subjected to tension forces as they resist the bending caused by the weight of the bridge deck and loads.
Together, compression and tension work to ensure the structural integrity and stability of the deck bridge.

## Slide 95: Load, compression and tension in bridges
The creation of the of the arch introduced the possibility of spanning great distances with higher bridges and greater clearance beneath them.
Photo by Cody Hiscox on Unsplash.
compression
Notes: Explain to learners:
Arch bridges work by transferring the load of the bridge deck and any additional weight (such as vehicles or pedestrians) to abutments (supports) at each end of the bridge. They utilise the unique structural properties of arches to distribute and support the load.
The load of the bridge deck and any additional weight placed on the bridge are transferred to the abutments or supports at each end of the bridge. The arch is the primary structural element of an arch bridge. It is a curved, semi-circular structure that spans across the gap to be bridged. The arch is designed to support the weight of the bridge deck by transferring the load horizontally to the abutments.
Arch bridges work primarily by utilising compression forces. When a load is applied to the bridge deck, the weight of the load exerts a downward force on the arch. This force is transmitted along the curve of the arch, resulting in compression forces that push against the abutments or supports.
The shape of the arch allows it to distribute the load evenly along its curve, thereby reducing the amount of stress on any single point. This distribution of load helps to minimise the risk of structural failure and ensures the stability of the bridge.
The abutments or supports at each end of the bridge are typically made of strong, durable materials such as concrete or masonry. They are designed to withstand the compression forces exerted by the arch and transfer the load to the ground or surrounding structures.
Additionally, the use of compression forces allows arch bridges to withstand heavy loads and external forces, such as wind and earthquakes.

## Slide 96: Load, compression and tension in bridges
Then the addition of multiple arches allowed bridges to span even further distances.
Photo by Jack Anstey on Unsplash.

## Slide 97: Watch the video
Watch the video “Bridge Design (and Destruction!) Part 1”.

## Slide 98: Load, compression and tension in bridges
The next development was the truss bridge. Constructing triangles of metal to form a truss created a structure that worked in combinations of compression and tension, was very strong, and could span even longer distances.
Photo by Ethan Finley on Unsplash.
tension
compression
Notes: Explain to learners:
A truss bridge works by distributing loads across a series of interconnected triangles, known as trusses, to efficiently support the weight of the bridge deck and any additional loads such as vehicles or pedestrians. Here’s how a truss bridge works:
The load of the bridge deck and any additional weight is transferred to the trusses, which are designed to distribute the load evenly across the bridge structure. Trusses are rigid structures composed of straight members (typically steel or timber beams) connected at joints. The arrangement of these members forms triangles, which are inherently stable and able to efficiently transfer loads.
Truss bridges utilise the principles of compression and tension forces. When a load is applied to the bridge deck, the weight exerts downward forces on the truss members. These forces are transmitted along the members, resulting in both compression and tension forces within the truss:
Compression: the upper members of the truss experience compression forces as they are pushed together under the load.
Tension: the lower members of the truss experience tension forces as they are pulled apart under the load.
The interconnected truss members create load paths that efficiently transfer the load from the bridge deck to the supporting abutments or piers.
The ends of the truss bridge are supported by abutments (at the ends of the bridge) or piers (if the bridge spans over a body of water). These supports are designed to withstand the vertical and lateral forces exerted by the truss bridge and transfer the loads to the ground or foundation.
Truss bridges are known for their stability and efficiency in supporting heavy loads over long spans. The triangular arrangement of truss members provides structural strength while minimising the amount of material needed, making truss bridges a cost-effective solution for spanning large distances.

## Slide 99: Load, compression and tension in bridges
The use of suspension bridges goes back many centuries. Some of the oldest are from the Incan era.
tension
compression
Photo by Gaetan Pautler on Unsplash
Notes: Explain to learners:
Suspension bridges have existed for many centuries – as far back as the Incan civilizations. The principle of a suspension bridge is the same as an arch bridge but inverted.
A suspension bridge works by utilising the tensile strength of its main cables to support the weight of the bridge deck and transfer loads to the supporting towers or pylons. Here’s how a suspension bridge works:
The primary structural elements of a suspension bridge are the main cables, which are large, strong cables made of steel wires bundled together. These cables run horizontally across the length of the bridge and are anchored securely at each end of the bridge. Tall towers or pylons are constructed to support the main cables. These towers or pylons are typically made of concrete or steel and are designed to withstand the tensile forces exerted by the main cables.
Vertical cables, known as suspenders, are attached to the main cables at regular intervals along the length of the bridge. These suspenders support the bridge deck and transfer the weight of the deck to the main cables. The bridge deck, which is the roadway or pedestrian path of the bridge, is suspended from the main cables by the suspenders. The deck hangs freely between the main cables and is not directly supported by the towers or pylons.
When a load, such as the weight of vehicles or pedestrians, is applied to the bridge deck, the load is transferred to the main cables through the suspenders. The main cables then transfer the load to the towers or pylons, which in turn transfer the load to the ground or foundation. The shape of the main cables between the towers or pylons forms a catenary curve, which is a natural curve that results from the distribution of tension along the cables. This curve helps distribute the load evenly and minimises stress on the cables and towers.
The tensile strength of the main cables allows the bridge to span long distances, while the flexibility of the cables and the catenary curve design help the bridge withstand external forces such as wind, seismic activity and temperature fluctuations.

## Slide 100: Load, compression and tension in bridges
The concept of stay cables, or stay girders, to support a bridge deck emerged in the mid-19th century. However, stayed bridges did not become widespread until the latter half of the 20th century.
Photo by João Silveira on Unsplash.
tension
compression
Notes: Explain to learners:
A stayed bridge transfers loads, experiences compression and tension forces, and maintains stability through a combination of its structural elements. Here’s how a stayed bridge works in terms of load transfer, compression and tension:
The load of the bridge deck and any additional weight (e.g. vehicles and pedestrians) are transferred to the bridge’s structural elements, including the deck itself and the supporting cables or girders.
Compression forces occur primarily in the bridge deck and the main structural components that support it. The weight of the bridge deck and any loads applied to it exert downward forces, causing compression within the deck and the supporting components such as beams or girders.
Tension forces primarily act on the stay cables or stay girders that support the bridge deck. Stay cables or girders extend diagonally from the deck to tall towers or pylons located adjacent to the bridge. When the deck is loaded, the weight creates tension forces in the stay cables or girders as they resist being pulled apart. The stay cables or girders are anchored to the towers or pylons, which also experience tension forces as they withstand the pull exerted by the stay cables or girders.
The load transfer mechanism in a stayed bridge involves the tension forces in the stay cables or girders counteracting the compression forces in the bridge deck and supporting components. The tension in the stay cables or girders stabilises the bridge deck, preventing excessive deflection or deformation under load.
The diagonal orientation of the stay cables or girders and their anchorage to tall towers or pylons enhance the bridge’s resistance to lateral forces, such as wind or seismic loads, contributing to its overall stability.

## Slide 101: Watch the video
Watch the video “Bridge Design (and Destruction!) Part 2”.

## Slide 102: Bridge-building activity
Using the theory of force, load, compression and tension, build a bridge with paper, string and sticky tape!

## Slide 103: Lesson summary quiz
What is the definition of force?
A
B

## Slide 104: Lesson summary quiz
What are two examples of external loads that structures may experience?
A
B

## Slide 105: Lesson summary quiz
What is the difference between dead load and live load?
A
B

## Slide 106: Lesson summary quiz
How can tension and compression be compared and contrasted?
A
B

## Slide 107: Lesson summary quiz
How does load transfer occur in a simple beam bridge?
A
B

## Slide 108: Lesson summary quiz
What is equilibrium?
A
B

## Slide 109: Lesson summary quiz
What are two types of loads that can affect a structure during an earthquake?
A
B

## Slide 110: Lesson summary quiz
What is uniform distributed load?
A
B

## Slide 111: 06
Earth science: weather and climate

## Slide 112: Weather and climate
What you will learn in this session:
the difference between weather and climate
how weather contributes to chemical degradation in metals.

## Slide 113: Weather charades
Complete the icebreaker activity:
Select a weather card.
Silently mime your weather to the class (or your partner).

## Slide 114: Weather and climate
Weather
  current conditions
  look out of the window!
  Photo by Vlad Chețan.
Climate
long-term trends
ranges and patterns of weather.
Photo by Engin Akyurt.
Notes: Explain to learners:
Weather and climate are often confused, but they have distinct meanings. Weather refers to the current state of the atmosphere, including temperature, humidity, precipitation, wind speed and atmospheric pressure. It is short-term and can change daily or even hourly. Climate, on the other hand, represents long-term average weather patterns over a specific region. It considers factors such as temperature ranges, rainfall patterns and prevailing winds, which remain relatively constant over extended periods.

## Slide 115: The weather cycle
The weather cycle refers to the continuous cycle of weather patterns that occur on earth.
It involves a series of processes such as the movement of air masses, the formation of clouds, precipitation, and the interaction between the atmosphere and the earth’s surface.
Notes: Explain to learners:
The weather cycle consists of several distinct phases: air masses moving across regions, the formation of clouds, condensation leading to precipitation and the dissipation of clouds. These phases occur in a continuous cycle, where air masses undergo fronts, such as cold fronts and warm fronts, leading to changes in temperature, pressure, humidity and wind patterns. These changes contribute to the overall weather conditions experienced in different areas.

## Slide 116: The weather cycle
Watch the video “What is weather, and how does it work?” by Learn Bright (8 minutes 4 seconds).
Answer the true or false questions using your true/false answer cards.

## Slide 117: The weather
Photo by Andrey Grinkevich on Unsplash
Photo by Jonathan Kemper on Unsplash
Photo by Max on Unsplash
Photo by Khamkéo Vilaysing on Unsplash
Sun
Rain
Wind
Temperature
Notes: Explain to learners:
The sun is the primary source of energy for our planet and plays a central role in the weather cycle. It provides heat and light, driving various atmospheric processes such as evaporation, condensation and temperature changes. The sun’s rays determine the intensity of weather patterns, influencing temperature variations and the occurrence of seasons.
Wind is the movement of air across the earth’s surface and plays a vital role in the weather cycle. It is caused by differences in atmospheric pressure and temperature. Wind affects the distribution of heat, moisture and pollutants, and it is responsible for shaping weather patterns. Winds may vary in intensity, direction and duration, influencing both local and global weather systems.
Rain is a vital component of the weather cycle. It occurs when water droplets in the atmosphere become heavy enough to fall to the earth’s surface. Rainfall replenishes water sources, nourishes vegetation and plays a significant role in the overall climate of an area. Different regions experience varying amounts of rainfall, contributing to diverse ecosystems across the globe.
Temperature is a crucial component of the weather cycle, representing the degree of hotness or coldness in the atmosphere. It fluctuates based on factors such as solar radiation, cloud cover and wind patterns. Temperature variations affect human comfort, plant growth and animal behaviour, ultimately shaping the overall weather conditions.
The sun itself does not directly deteriorate metals. Its effects on temperature, moisture, chemical reactions and protective coatings indirectly contribute to metal deterioration and corrosion over time.

## Slide 118
The influence of temperature on sunlight intensity:
As temperature increases, the air is less dense, and more sunlight can get through.
As temperature decreases, the air is denser, and less sunlight can get through.
The weather
Notes: Explain to learners:
Temperature has a direct influence on sunlight intensity. As the temperature increases, the air becomes less dense, causing the light to encounter fewer particles, leading to less scattering. This results in higher sunlight intensity. On the other hand, colder temperatures increase the density of the air, leading to increased scattering and reduced sunlight intensity.
Thus, it is evident that temperature directly affects sunlight intensity, playing a crucial role in determining the amount of solar radiation reaching the earth’s surface.

## Slide 119: The weather
The impact of sunlight duration on temperature changes:
Variations in sunlight duration directly contribute to temperature fluctuations in different regions across the globe.
Image by Arek Socha from Pixabay.
Notes: Explain to learners:
Sunlight duration plays a significant role in determining temperature changes. The amount of sunlight received in a particular region affects the warming and cooling of the earth’s surface. As the duration of sunlight increases, more solar energy is absorbed by the earth’s surface, leading to higher temperatures. Conversely, shorter sunlight duration results in less solar energy absorption, causing cooler temperatures.
Variations in sunlight duration directly contribute to temperature fluctuations in different regions across the globe.

## Slide 120: The weather
greenhouse gas emissions
increased global temperatures
changes in sunlight patterns.
Photo by Peggy Anke on Unsplash.
The impact of temperature and sunlight on climate change:
Notes: Explain to learners:
Temperature and sunlight have a significant impact on climate change. Increased global temperatures, influenced by factors such as greenhouse gas emissions, can lead to changes in sunlight patterns. Changes in sunlight duration can disrupt ecosystems, alter weather patterns and affect the balance of earth’s climate system. Similarly, alterations in sunlight intensity, caused by variations in temperature, can further exacerbate climate change. This interplay between temperature and sunlight is critical to understanding the complex relationship between these factors and their contribution to global climate change.

## Slide 121: The weather
Images from the “Understanding Global Change” project, University of California Museum of Palaeontology, 2024.
Transportation of heat and moisture
Notes: Explain to learners:
Wind plays a crucial role in the transportation of heat and moisture across the earth’s surface, leading to changes in weather patterns. When warm air rises, it creates an area of low pressure, causing cooler air from surrounding regions to rush in and replace it. These air movements, known as convection currents, help distribute heat and moisture around the planet. By transferring warm air from the equator to the poles and vice versa, wind helps regulate global temperature and contributes to the formation of different weather systems.

## Slide 122: The weather
Formation of weather systems
Understanding the influence of wind on weather system formation is crucial for meteorologists in predicting and analysing weather conditions.
Image by clker-free-vector-images from Pixabay.
Notes: Explain to learners:
Wind is a primary factor in the formation of weather systems. When air masses with different temperatures and humidity levels collide, they create atmospheric disturbances that lead to the development of various weather patterns. For instance, the collision of a warm air mass and a cold air mass can result in the formation of a low-pressure system, which often causes storms and precipitation. The interaction of wind speeds and directions determines the intensity and movement of weather systems, including hurricanes, tornadoes and thunderstorms. Understanding the influence of wind on weather system formation is crucial for meteorologists in predicting and analysing weather conditions.

## Slide 123: The weather
Wind has a significant impact on local weather conditions, shaping day-to-day weather patterns in specific regions.
Image by cromaconceptovisual from Pixabay.
Local weather effects
Notes: Explain to learners:
Wind has a significant impact on local weather conditions, shaping day-to-day weather patterns in specific regions. The topography, such as mountains, hills and bodies of water, can modify wind directions and speeds, leading to localised weather effects. For example, when air encounters a mountain range, it is forced to rise, resulting in condensation and the formation of clouds and precipitation on the windward side. On the leeward side, the descending air tends to be drier and warmer, often leading to clearer skies and less precipitation. Locally, wind can also influence temperatures, air quality and the behaviour of weather phenomena like fog or sea breezes.

## Slide 124: The weather
Topographical effects
Landforms also play a significant role in the influence of wind on weather patterns.
Photo by Mathias Reding on Unsplash.
Notes: Explain to learners:
The presence of different landforms also plays a significant role in the influence of wind on weather patterns. Topographical features, such as valleys, canyons and plateaus, affect wind speed and direction, impacting local weather conditions. For example, a narrow valley can act as a funnel, accelerating the wind and leading to stronger gusts. Topographic barriers can also cause air to be lifted or forced down, triggering changes in temperature, humidity and cloud formation. By interacting with the earth’s topography, wind creates microclimates, influencing weather patterns and conditions in specific areas.

## Slide 125: The weather
Wind-driven ocean currents are closely connected to weather patterns.
Photo by frank mckenna on Unsplash.
Notes: Explain to learners:
Wind-driven ocean currents are closely connected to weather patterns. When wind blows over the ocean’s surface, it generates friction and transfers some of its energy to the water, creating surface currents. These currents, driven by wind patterns and the earth’s rotation, distribute heat around the world’s ocean basins, influencing the climate of coastal areas. Warm ocean currents tend to bring milder and wetter weather to nearby land, while cold ocean currents can result in cooler and drier conditions. Understanding the relationship between wind and ocean currents is essential for predicting long-term climate trends and studying the impact of climate change.

## Slide 126: Weather and deterioration research
Research task:
Complete the research on your topic.
Find your research partner.
Create a presentation or poster to share your research with the class.

## Slide 127: 07
Running an experiment

## Slide 128: Running an experiment
What you will learn in this session:
how to make predictions
how to set up and run a weather experiment.

## Slide 129: Predicting outcomes
Prediction
versus
Assumption
Notes: Explain to learners:
Predictions are educated guesses about what might happen during an experiment based on prior knowledge and understanding of the topic being explored.
Making a scientific prediction involves saying what might happen during or at the end of the experiment. Predictions often relate to an if/then scenario, for example, if “y” increases, then “x” might happen. The “x” is based on knowledge and is not an assumption.
Assumptions do not have any substantial truth and are taken as facts without evidence to support them.
In science, it is important that outcomes to experiments are predicted rather than assumed, as this can result in inaccurate data.

## Slide 130: Predicting outcomes
The importance of predicting outcomes:
Predictions help focus the experiment by setting clear objectives.
They provide a framework for collection of data and analysis.
Predictions allow evaluation of the success or failure of the experiment based on expected outcomes.

## Slide 131: Predicting outcomes
Independent variables are the variables being changed during the experiment.
Dependent variables are the variables being tested or measured during the experiment.
Image by clker-free-vector-images from Pixabay.
Notes: Explain to learners:
Within an experiment, there are variables. These are the things that can change and be measured. There are two types of variables that can help make predictions.
Independent variables are the variables being changed during the experiment.
Dependent variables are the variables being tested or measured during the experiment.
In an experiment where different metals are exposed to different temperatures and levels of humidity, the temperature and humidity are independent variables. These can both be changed and measured.
The dependent variable is what is then observed in the metals when the change is made, for example the rate of corrosion or colour change.
Understanding the variables helps guide the predictions that can be made.

## Slide 132: Predicting outcomes
How to predict outcomes:
Review the background information and existing knowledge.
Formulate a hypothesis based on this information.
Consider the variables and potential outcomes.
Use evidence and logic to support your predictions.
Consider the alternative outcomes and possible limitations of the predictions.
Notes: Explain to learners:
There is a process to making predictions. They are considered in the following stages.
1. Review background information and existing knowledge: before making predictions, it’s essential to gather relevant background information and tap into existing knowledge related to an experiment. This involves studying previous research, theories, principles and any relevant literature or data available. Reviewing background information helps to develop a solid understanding of the topic and its underlying principles, which will inform predictions.
2. Formulate hypotheses based on information: a hypothesis is an educated guess about what will happen in the experiment. Based on the background information reviewed, hypotheses can be created that serve as the foundation for any predictions. Hypotheses should be clear, specific and based on logical reasoning derived from the available information.
3. Consider variables, potential outcomes and expected trends: by identifying and analysing the variables involved in the experiment, reasonable expectations regarding expected changes in the variables can be made, including how they may impact the outcomes of an experiment. By evaluating potential outcomes and any expected trends, learners can anticipate how different factors might interact and influence the results.
4. Use evidence and logic to support predictions: predictions should be based on logical reasoning and supported by evidence from the background information and hypotheses. Use deductive reasoning to draw conclusions from the available evidence and formulate predictions. Consider cause-and-effect relationships, patterns and logical connections between variables to justify predictions.
5. Consider alternative outcomes and potential limitations: it’s important to acknowledge that experiments are subject to variability and uncertainty, leading to alternative outcomes. Consider possible alternative scenarios or unexpected results that could arise during the experiment. Also consider potential limitations of the predictions, such as incomplete data, experimental errors or uncontrolled variables, and how these factors might affect the reliability of any predictions.

## Slide 133: Predicting outcomes
Predicting weather:
collect quantitative data
forecast using historical data
predict using climatic changes over time
validate.
Notes: Note to teacher:
Images taken from pexels.
Explain to learners:
Meteorologists collect data from various sources such as satellites, weather stations, buoys and radar systems. This data includes temperature, humidity, air pressure, wind speed and direction, cloud cover, and precipitation – all the elements of current knowledge that can influence future weather.
Forecasting takes place by comparing this data with historical data, known weather events and physical laws governing atmospheric dynamics.
Predictions are made by calculating changes over time based on conditions and analysing historical climatic data to identify patterns and trends, such as seasonal variations and climate oscillations. Multiple simulations with slight variations in initial conditions are surmised to account for uncertainty and provide a range of possible outcomes, along with probabilities for different weather scenarios.
Validation of the process takes place when meteorologists continuously monitor and verify forecast accuracy by comparing predicted conditions with observed weather.

## Slide 134: Predicting outcomes activity
If all the balls drop from the same height…
Which will hit the ground first?
Which will drop fastest?
Notes: Notes to teacher:
Images taken from unsplash and pexels.
Take a table-tennis ball, tennis ball, cricket ball and a football and ask the learners, “If all the balls drop from the same height, which will hit the ground first?”
Allow learners a few minutes to suggest answers, then challenge the answers by asking, “How do you know that?” Engage discussion for a few minutes, then explain that their comments are assumptions and that the process of predicting outcomes can be applied to make an educated guess and predict the outcome.
Use the Predicting outcomes activity instructions in the lesson plan to explain to learners what each group will do to form the prediction.

## Slide 135: Predicting outcomes activity
Writing the predictions:
In your groups, complete the task and worksheet you are allocated.
Write your predictions for each ball.

## Slide 136: Running an experiment: metal deterioration experiment
Set up your experiment as directed in the instructions.
Complete the predictions stages of the activity.
Complete the sections of the report template.

## Slide 137: Running an experiment: windy day simulation and frost formation
Set up your experiment as directed in the instructions.

## Slide 138: Running an experiment: solar heat experiment
Set up your experiment as directed in the instructions.
Take readings at five-minute intervals.
Conduct research into real-world applications for this knowledge.

## Slide 139: 08
Force and load calculations

## Slide 140: Force and load calculations
What you will learn in this session:
calculations of force, load and reactions.

## Slide 141: Equilibrium recap
If an object is stationary, it is in a state of equilibrium.
Equilibrium is the state of an object where all the forces acting on the structure are in balance and no movement occurs.
The sum of forces (including support reactions) must be zero in both horizontal and vertical directions (shear) and torque (bending moment).

## Slide 142: Equilibrium recap
Notes: Explain to learners:
The sum of all the vertical forces should equal zero.
The sum of all the horizontal forces should equal zero.
The sum of all the moment forces should also equal zero.

## Slide 143: Shear force calculations
F1
F2
F3
BEAM
R1
R2
R1 + R2 = F1 + F2 + F3
Notes: Explain to learners:
Consider the beam shown.
The beam is supported by columns at each end. There must be force at these points to maintain the equilibrium – these are called the reaction forces and will be referred to with the notation “R”.
It also supports downward vertical loads F1, F2 and F3 at various points along its length.
Where there are downward forces, there must be equal, opposing upward forces (reactions) and using knowledge of vertical equilibrium we know that the total force down must be equal to the total force up.
The summary is then that: R1 + R2 = F1 + F2 + F3.

## Slide 144: Shear force calculations
F1
F2
F3
R1
R2
30kN
5kN
5kN
BEAM
25kN
15kN
R1 + R2 = F1 + F2 + F3
25kN + 15kN = 30kN + 5kN + 5kN
40kN = 40kN
Notes: Explain to learners:
If the F and R notation is substituted for values…
Click for next action.
It is apparent that the downward “F” forces, added together, will equal all the upward ‘R’ forces.
Click for next action.

## Slide 145: Shear force calculations
-30kN
-5kN
-5kN
+25kN
-15kN
BEAM
A
2m
1m
2m
1m
Shear force at A = +25 -30 -5 -5 = -15kN
Notes: Explain to learners:
Having established that the whole beam is in shear equilibrium, it is possible to calculate the shear forces at any given point along the beam if the distances for the force applications are known.
To calculate the shear force at point A, ignore everything to the right of A and examine all the forces that exist to the left of A.
Remind learners that clockwise action is positive and anticlockwise is negative.
This solution is -15kN, which we can see is correct because we know the reaction to the right of fixed-point A is -15kN.

## Slide 146: Shear force calculations activity
Instructions:
Complete shear force calculations worksheet.
Check your answers.

## Slide 147: Bending moment calculations
d
F
A
F
d
A
Notes: Explain to learners:
A moment is a turning effect. A moment always acts about a given point and is either clockwise or anticlockwise.
The moment about point A, caused by a particular force F, is defined as the force F multiplied by the perpendicular distance from the force’s line of action to the point (d).
Units of moment are kN.m (kilonewton metres). This is because a moment is a force multiplied by a distance.
In both cases shown, if M is the moment about point A, then M=Fx.
It is much easier to undo a bolt if a long spanner is used rather than a short one. This is because, although the force used may be the same, the lever arm distance is longer, thus causing a greater turning effect or moment to be applied.
It is also important to distinguish between clockwise and anticlockwise moments. After all, turning a spanner clockwise (tightening a nut) has a very different effect from turning the spanner anticlockwise (loosening the nut).
Clockwise moments are regarded as positive (+).
Anticlockwise moments are regarded as negative (-).

## Slide 148: Equilibrium and bending moments activity
The formula for calculating the bending moment or torque is:
τ = F × D
Where:
τ = torque (measured in Newton-metres or Nm)
F = force applied (measured in Newtons or N)
D = perpendicular distance from the force to the pivot point (measured in metres or m).
Notes: Explain to learners:
The bending moment is sometimes called the turning force and is torque – i.e. it is a measure of how effectively a force can cause an object to rotate around an axis or pivot point.
In this experiment, torque is the product of the force (weight of the coin) and the perpendicular distance from the force to the pivot point. Using the equation τ = F × D allows engineers to calculate the anticipated bending moment at any given point along a beam.

## Slide 149: Equilibrium and bending moments activity
τ = F × D
τ total​ = 0.05N × 0.1m
τ total​ = 0.005Nm
0.1m
0.05N
Notes: Explain to learners:
To calculate the torque exerted by a coin on the ruler, multiply the weight of the coin by its distance from the pivot point.
For example, if a coin has a weight of 0.005 kg (equivalent to 0.05 N in earth’s gravitational field) and is positioned 0.1 metres from the pivot point, the torque exerted by the coin would be:
0.05N × 0.1m =0.005Nm (weight multiplied by distance)

## Slide 150: Equilibrium and bending moments activity
τ total​ = (0.05N × 0.1m) + (0.05N × 0.2m) + (0.05N × 0.3m)
τ total = 0.005 + 0.01 + 0.015
τ total​ = 0.005Nm + 0.01Nm + 0.015Nm
τ total​ = 0.03Nm
0.1m
0.2m
0.3m
0.05N
0.05N
0.05N
?
?
Notes: Explain to learners:
For the ruler to remain in equilibrium (balanced and level), the total torque exerted by the coins on one side of the pivot point must equal the total torque exerted by the coins on the other side.
So, if there are three coins on one side of the ruler, each with a weight of 0.005 kg (0.05 N) and positioned 0.1 metres, 0.2 metres and 0.3 metres from the pivot point respectively, all their torques added together will give us the total torque.
This then lets us know how much force to use and where we need to place it to create equilibrium.
Using this method, it can be calculated where to place coins on the ruler and how many to place to create balance and equilibrium on the ruler.

## Slide 151: Equilibrium and bending moments activity
Instructions:
Balance the ruler on the pivot so it is flat.
Add equal weights to each end, keeping the ruler flat.
Now move one set of weights closer to the pivot point. Remove weights as needed to maintain balance (equilibrium).
Note the distance on the ruler and the amount of weight needed to retain the balance.
Repeat at different distances from the pivot point.

## Slide 152: Bending moment calculation example 1
2m
4kN
A
M = 4kN x 2m = 8kN.m
Notes: Explain to learners:
The 4kN force is trying to turn clockwise about point A, therefore the moment will be +ve.
The 2m distance is measured horizontally from the (vertical) line of action of the 4kN force; in other words, the distance given is measured perpendicular to the line of action of the force.

## Slide 153: Bending moment calculation example 2
2m
3m
4kN
A
5kN
M = (5kN x 3m) + (4kN x 2m) = 23kN.m
Notes: Explain to learners:
This time there are two forces, supplying two moments. A common mistake with this example is to assume that since the two forces are in opposite directions, the moments must also oppose each other. On closer inspection they are both +ve.

## Slide 154: Bending moment calculation example 3
M = (7kN x 4m) + (98kN x 0m) = 28kN.m
4m
98kN
A
7kN
Notes: Explain to learners:
Once again, there are two forces supplying two moments. The 7kN force gives rise to a clockwise moment. The 98kN force, however, passes straight through pivot point A. In other words, its line of action is zero from A. Since a moment is always a force multiplied by a distance, if the distance is zero then it follows that the moment must be zero.

## Slide 155: Bending moment calculation example 4
M = (-6kN x 3m) = -18kN.m
A
3m
6kN
Notes: Explain to learners:
The 6kN force is turning anticlockwise about A, so the resultant moment will be negative (-ve).

## Slide 156: Bending moment calculation example 5
M = (5kN x 3m) - (2kN x 5m) = 5kN.m
3m
2m
5kN
2kN
A
Notes: Explain to learners:
The 5kN force is trying to turn clockwise about A and therefore will give rise to a +ve moment. By contrast, the 2kN force is trying to turn anticlockwise about A, giving rise to a -ve moment.

## Slide 157: Bending moment calculation example 6
M = - (6kN x 5m) = -30kN.m
5m
A
6kN
Notes: Explain to learners:
Not all forces are vertical – but the same rules apply.

## Slide 158: Bending moment calculation example 7
A
3.2kN
5m
Y = vertical component of force
X= horizontal component of force
53.1°
Notes: Explain to learners:
Sometimes the force is applied at an angle – in this case it is necessary to find the perpendicular aspect of the force that is being applied.

## Slide 159: Bending moment calculation example 7
A
3.2kN
5m
53.1°
53.1º
3.2 kN
x kN
Horizontal force
CAH
Cos 53.1° = x /3.2kN
Cos 53.1° x 3.2kN = x
x = 0.6 x 3.2kN
x = 1.92kN
Notes: Explain to learners:
Using trigonometry ratios and the SOH CAH TOA mnemonic, the angled load can be split into its vertical and horizontal components.
Here, the cosine of 53.1° being used as the adjacent side to the angle is the unknown quantity and the hypotenuse is the known value.

## Slide 160: Bending moment calculation example 7
A
1.28kN
5m
1.8kN
M = (1.28kN x 5m) + (1.8kN x 0)
M = 6.4kN.m
Vertical force
Total force = 3.2kN
3.2kN – 1.92kN = 1.28kN
Notes: Explain to learners:
Using trigonometry ratios and the SOH CAH TOA mnemonic, the angled load can be split into its vertical and horizontal components.
The vertical force can be calculated by deducting the horizontal element of the force from the total force and the moment calculation can now be completed.

## Slide 161: Bending moment calculations activity
Instructions:
Complete the bending moment calculation worksheet.
Check answers.
Notes: Explain to learners:
Sometimes the force is applied at an angle – in this case it is necessary to find the perpendicular aspect of the force that is being applied.

## Slide 162: Reaction calculations
F1
F2
F3
BEAM
R1
R2
Notes: Explain to learners:
The reaction counteracts the (usually downward) forces in the structure to maintain equilibrium.
It is important to be able to counteract these reactions. If the support is a column, for example, the reaction represents the force in the column, which we would need to know to design the column.

## Slide 163: Reaction calculations
18kN
A
B
4m
2m
R1
R2
R1 + R2 = 18kN
Notes: Explain to learners:
Consider the example shown. The beam spans 6m, which is simply supported at ends A and B. The only load on the beam is a point load of 18kN, which acts vertically downwards at a position 4m from point A.
We need to calculate the reactions R1 and R2.
We already know that the total upward force = total downward force:
R1 + R2 = 18kN
This doesn’t tell us the value of R1 or R2, but using the calculation of moments and knowing that clockwise moments need to equal anticlockwise moments for equilibrium to exist, this can be calculated.

## Slide 164: Reaction calculations
Using our knowledge of moment equilibrium, total clockwise moment = total anticlockwise moment.
Calculating moments around fixed point A:
18kN x 4m (clockwise) = R2 x 6m (anticlockwise)
B
4m
2m
A
18kN
R1
R2
12kN
18kN x 4m = R2 x 6m
18kN x 4m = R2
6
RB = 12kN
Notes: Click for actions to explain each part of the calculation.

## Slide 165: Reaction calculations example
2m
1m
15kN
10kN
2m
1m
30kN
25kN
Bending moments at A = (+25kN x 4m) – (30kN x 2m) – (10kN x 1m) – (15kN x 2m)
= 100kNm – 60kNm – 10kNm – 30kNm
= 0kNm
A
2m
1m
15kN
10kN
2m
1m
30kN
25kN
2m
1m
15kN
10kN
2m
1m
30kN
25kN
2m
1m
15kN
10kN
2m
1m
30kN
25kN
2m
1m
15kN
10kN
2m
1m
30kN
25kN
Notes: Click for actions to explain each part of the calculation.
Explain to learners:
Using bending moments and reaction calculations can demonstrate that the beam is in equilibrium.

## Slide 166: Reaction calculations example
Bending moments at B clockwise = anticlockwise
(-10kN x 3m) + (-30kN x 4m) = (R1 x 6m)
-30kNm -120kN = R1 x 6m
-150kN/ 6m = R1
-25kN = R1
2m
1m
R2
10kN
2m
1m
30kN
R1
A
B
Notes: The same principle can be used to find unknown reactions.
By calculating known bending moments around either end of the beam, the value of one of the reactions can be determined and then, using the principle of all verticals being equal, the other can be calculated.
Click for actions to explain each part of the calculation.

## Slide 167: Reaction calculations activity
Instructions:
Complete the Reactions calculations worksheet.
Check your answers.
Notes: Explain to learners:
Sometimes the force is applied at an angle – in this case it is necessary to find the perpendicular aspect of the force that is being applied.

## Slide 168: 09
Analysing experimental data

## Slide 169: Analysing experimental data
What you will learn in this session:
how to conclude the nail deterioration experiment
how to analyse experimental data.

## Slide 170: Concluding an experiment
data organisation
evaluation of effects
comparison of results
hypothesis confirmation
discussion of findings
recommendations
presentation of conclusions.
Notes: Explain to learners:
When an experiment is completed, there is information. The next step is to do something with this information. Every experiment has an objective at the outset – i.e. what was the purpose of the experiment? What was being established? What questions were being answered?
In the metal deterioration experiment, the objective was “To investigate the impact of varying environmental conditions, including exposure to different fluids and weathering, on the chemical degradation of metals over a period of four weeks.” The typical observations being made were:
no visible changes
some surface discoloration
slight corrosion (appearance of rust, for example)
greenish patina formation
minor tarnishing (loss of brightness, dull appearance)
liquid colour.
There should now be lots of information about the metals over the time period, exploring what happens to the metals while they are exposed to different conditions.
Through the following process, an experiment can move from being completed and having available data, to being communicable to a wider audience.
Data organisation: begin by organising the data collected during the experiments. This may include measurements of corrosion rates, changes in material properties, visual observations and any other relevant data points.
Comparison of results: compare the results obtained from different environmental conditions and weather phenomena. Look for patterns, trends and differences between the samples exposed to various conditions.
Evaluation of effects: assess the effects on the different types of metals. Determine if certain metals are more susceptible to degradation in particular environments or under specific conditions.
Comparison of results: compare the results obtained from different conditions. Look for patterns, trends and differences between the samples exposed to various conditions.
Hypothesis confirmation: evaluate whether the experimental results support the initial predictions formulated before conducting the experiments. If the data aligns with the hypotheses, consider them confirmed. If not, refine the hypotheses based on the observed outcomes and maybe do the experiment again.
Discussion of findings: discuss the significance of the findings in the context of construction materials and infrastructure durability. Highlight the implications for designing structures to withstand environmental challenges and potential strategies for mitigating corrosion in real-world applications.
Recommendations: based on the conclusions drawn from the experiments, make recommendations for further research or practical applications. These recommendations may include suggestions for selecting appropriate materials, implementing protective coatings or designing structures to minimise exposure to corrosive environments.
Presentation of conclusions: present the conclusions of the experiments in a clear and concise manner, supported by relevant data and analysis. Use visual aids, such as graphs, charts and photographs, to enhance understanding and communicate key findings effectively. Select the most suitable means to present your work. Sometimes a formal report is needed but other times an infographic may be more appropriate for the audience.

## Slide 171: Concluding an experiment
Data organisation
Image by StartupStockPhotos from Pixabay
Notes: Explain to learners:
Organising experimental data efficiently is crucial because it aids in minimising errors, ensuring consistency, promoting data integrity and fostering an effective teamwork environment. The stakes rise when disorganised data causes loss of vital information, inaccuracies or difficulties in reproducing results.
Effective organisation of experimental data has many benefits, among which saving time on data management, enhancing the accuracy of results and facilitating efficient collaboration between team members are most important. Depending on the volume and complexity of the data, the nature of the experiments, the level of collaboration and the requirements of the data regulators, the goals of organising experimental data could vary.
In the metal deterioration experiment, there were six metals in four environments being observed over four weeks, so it makes sense that each week is recorded separately to be able to demonstrate progression of the deteriorations over the time period.

## Slide 172: Concluding an experiment
Evaluation of effects
Notes: Explain to learners:
Before making any conclusive comments about the deterioration of the metals, the quality of the data gathered must first be evaluated.
Data from the observations must be scrutinised to reject any random errors. These may be results that are questionable because of interference with the experiment or method of observation. For this reason, it is often advisable to take photographs at every observation time.
At the end of an experiment, it is important to evaluate the results and the method. After this is done, a judgement is made about how reliable the conclusion is. Improvements to the method should be suggested and then an explanation should be given as to how this would lead to data of a better quality.

## Slide 173: Concluding an experiment
Comparison of results
Image by Clker-Free-Vector-ImagesPixabay
Notes: Explain to learners:
Comparison of results: compare the results obtained from different conditions. Look for patterns, trends and differences between the samples exposed to various conditions.
In the metal deterioration experiment, look for similar occurrences between differing metals I the same liquids. Are there any common factors?

## Slide 174: Concluding an experiment
Hypothesis confirmation
Notes: Explain to learners:
Hypothesis confirmation: evaluate whether the experimental results support the initial predictions formulated before conducting the experiments. If the data aligns with the hypotheses, consider them confirmed. If not, refine the hypotheses based on the observed outcomes and maybe do the experiment again.

## Slide 175: Concluding an experiment
Presentation of conclusions
Notes: Explain to learners:
Present the conclusions of the experiments in a clear and concise manner, supported by relevant data and analysis. Use visual aids such as graphs, charts and photographs to enhance understanding and communicate key findings effectively. Select the most suitable means to present your work. Sometimes a formal report is needed but other times an infographic may be more appropriate for the audience.

## Slide 176: Concluding an experiment
Discussion of findings
Notes: Explain to learners:
Discussion of findings: discuss the significance of the findings in the context of construction materials and infrastructure durability. Highlight the implications for designing structures to withstand environmental challenges and potential strategies for mitigating corrosion in real-world applications.
A conclusion says what has been found out during an investigation. A good conclusion does the following:
fully describes the relationship between variables
links the findings back to the hypothesis
explains findings using scientific knowledge and understanding.
In the metal deterioration experiment, the underpinning science for any deterioration is chemical reactions between the metals and the liquids. Review the “think, pair, share” activity in lesson 6 for more information about the chemical reactions taking place here.

## Slide 177: Concluding an experiment
Recommendations
Image by AlexMile from Pixabay
Notes: Explain to learners:
Based on the conclusions drawn from the experiments, make recommendations for further research or practical applications. These recommendations may include suggestions for selecting appropriate materials, implementing protective coatings or designing structures to minimise exposure to corrosive environments.
The recommendations can also be to repeat the experiment to confirm the findings or to undertake another experiment to explore more options or ideas.

## Slide 178: Sharing experiment observations
Prepare your observation data ready for sharing with the class.
Share the data, explaining the observations briefly.
Notes: Explain to learners:
Because each group only considered one metal, it is necessary to share the observations with the rest of the class so each person can complete the report fully.

## Slide 179: Complete the metal deterioration experiment report
Using the Metal deterioration experiment report template started in lesson 7, complete your report for the experiment.

## Slide 180: 10
Informed decision-making

## Slide 181: Recap: Using data to make informed decisions
What you will learn in this session:
informed decision-making
using data to make metal specifications in constructions.

## Slide 182: Recap: Using data to make informed decisions
What has been learnt?
properties of metals
behaviour associated with those properties
effects of applied force and load
calculations to demonstrate failure or equilibrium.
Notes: Recap for learners lessons 1, 2, 3, 4, 5 and 8.

## Slide 183: Recap: Using data to make informed decisions
What has been learnt?
weather and climate
the effect of these on metals when exposed
types of degradation that occur in metals when exposed.
Notes: Recap for learners lessons 6 and 7.

## Slide 184: Using data to make informed decisions
Concluding scenario one:
In pairs, consider the scenario you have been given.
Use the scenario to answer the questions.
Notes: Recap for learners lessons 6 and 7.

## Slide 185: Using data to make informed decisions
Concluding scenario two:
In pairs, consider the scenario you have been given.
Use the scenario to answer the questions.

## Slide 186: Using data to make informed decisions
Concluding scenario three:
In pairs, consider the scenario you have been given.
Use the scenario to answer the questions.

## Slide 187: ET-FOUNDATION.CO.UK
PRODUCED BY
Ruth Brown at
FUNDED BY
This programme is funded by the Department for Education
Leeds College of Building has produced this resource on behalf of the Education and Training Foundation