## Slide 1: Introduction to engineering mechanics – Session 1
Hugh Baird College
Time and date
Location

## Slide 2: 01
Introduction to today’s session outcomes

## Slide 3: Today’s session outcomes
Overview of the course
Problem-based learning approach (PBL)
Structural features of systems
Constructing free body diagrams (FBD)
Understand and calculate forces in static systems using Newton’s laws
Understand and calculate forces and accelerations using Newton’s laws
Introduction to next session

## Slide 4: Seven-week course introduction
Course to support the understanding of science concepts in the T Level in Engineering and Manufacturing core content.
An automated overhead crane system is used to teach the science concepts in Mechanical, Electrical and Electronic, Control and Instrumentation and Structural Engineering occupational specialisms.
The course covers modelling and analysis of static equilibrium and dynamic problems with an emphasis on real-world applications and problem solving.

## Slide 5: Links of the course to the overall T Level programme
Core components

## Slide 6: Course sessions
Free body diagrams and equilibrium analysis techniques
Types of forces on simply supported (SS) beams
Shear force and bending moment analysis of simply supported beams
Principle of conservation of momentum
Principle of conservation of energy
Power in mechanical systems
Types of power sources

## Slide 7: How and when this will be assessed
This course focuses on elements of the core content which is assessed by:
Core examinations
Employer-set project (ESP)

## Slide 8: 02
Problem-based learning approach (PBL) project

## Slide 9: True or false assessment questions
We will be learning about electrical principles.
The content will be assessed in core examinations.
We will be learning about Newton’s laws.
True
False
True
False
True
False
Notes: False
True
True

## Slide 10: PBL project
Problem-based learning (PBL) gives the opportunity to solve open-ended, real-work problems.
We will be analysing an automated overhead crane system using the principles learnt on the course.

## Slide 11: Structural components
What are the structural components of this building?
What are the structural components of the system in the video?
Physical elements that support or transfer the forces

## Slide 12: Automated overhead crane in operation – 1
(639) EOT Crane | Double Girder | Overhead Crane | EOT Crane Working | How Crane Works? | 3D Animation – YouTube

## Slide 13: Automated overhead crane in operation – 2
(639) Single Girder vs. Double Girder Bridge Overhead Crane Design | L2–S1 – YouTube
Notes: At the end of the video, discuss the answers for the pre-video question on slide 11.

## Slide 14: 03
Free body diagrams

## Slide 15: Construct free body diagrams (FBD)
The first step in solving problems involving Newton’s laws is to draw the FBD.
Let’s watch this video and list the FBD construction steps.
(639) Free-Body Diagrams - YouTube

## Slide 16: Construct free body diagrams (FBD)
Steps to construct FBD
Identify the specific object.
Isolate it from the rest of the objects.
Draw the system boundary line to identify any field forces acting on the object – optional.
Draw all external forces acting on the body using arrows.

## Slide 17: Example FBD 1
Mg
N

## Slide 18: Example FBD 2
R1
R2
F
Rc
W

## Slide 19: Your turn to draw a FBD

## Slide 20: Answer to FBD of the box
F2
Mg
N
F1

## Slide 21: Construct FBD for the automated double girder overhead crane in operation – 1 shown in slide 12
(639) EOT Crane | Double Girder | Overhead Crane | EOT Crane Working | How Crane Works? | 3D Animation - YouTube

## Slide 22: Forces that should be considered for the FBD of double girder AOC
Tension
Thrust/pull
Friction force
Reaction force
Reaction force
Reaction force
Reaction force
Weight
Weight
Weight
*Important: The AOC system is considered as an indoor structure here, to avoid the effects from forces generated due to wind.
**Note that this diagram should not be considered as an FBD. This only contains the type of forces that should be considered for the construction of FBD.

## Slide 23: 04
Newton’s laws

## Slide 24: Newton’s first law (Law of inertia)
An object at rest tends to stay at rest and an object in motion tends to stay in motion unless acted upon by an unbalanced force.
https://www.bbc.co.uk/bitesize/guides/zqs47p3/revision/1

## Slide 25: Mass and inertia
Every object continues in its state of rest, or uniform motion in a straight line, unless it is compelled to change that state by unbalanced forces impressed upon it.
Inertia is a property of objects to resist changing its motion.
Mass is a measure of the amount of inertia.
Mass is a measure of the resistance of an object to changes in its velocity.
Mass is an inherent property of an object.
It is a scalar quantity and uses the SI unit kg.

## Slide 26: Newton’s second law (Law of motion)
The acceleration of an object is directly proportional to the net force acting on it and inversely proportional to its mass.

## Slide 27: More about Newton’s second law
Newton’s second law:
SI unit of force is a Newton (N)

## Slide 28: More about Newton’s second law
You must be certain about which body we are applying it to.
must be the vector sum of all the forces that act on that body.
Only forces that act on that body are to be included in the vector sum.
The net force component along an axis gives rise to the acceleration along that same axis.

## Slide 29: Newton’s third law (Action–reaction)
For every action there is an equal and opposite reaction.

## Slide 30: More on Newton’s third law
Equivalent to saying a single isolated force cannot exist.

## Slide 31: More on Newton’s third law
Equivalent to saying a single isolated force cannot exist
Pull
Pull
Tension
Tension

## Slide 32: True or false assessment questions
No resultant force is acting on the planet Mars.
A free-falling accelerating object has a resultant force.
A free-falling object always has a resultant force.
True
False
True
False
True
False
Notes: False
True
False

## Slide 33: Example 1
What is the magnitude of the force that is exerted on a 25 kg mass to give it an acceleration of 10.0 m/s2?
Assume a frictionless surface.
F
10.0
Mg
Ans: 250 N
Notes: Answer: F = ma, F = 25 x 10 = 250 N

## Slide 34: Example 2
What is the magnitude of the acceleration that is produced when the brakes of a car are applied with a force to stop the car?
Mg
Force
Velocity
Ans: 1.5 m/s2
Notes: Answer: a = F/m, a = (3.6 x 1000 )/(2.4 x 1000) = 1.5 m/s2

## Slide 35: Hints for problem solving
  Read the problem carefully at least once.
  Draw a picture of the system, identify the object of primary interest, and indicate forces with arrows.
  Label each force in the picture in a way that will bring to mind what physical quantity the label stands for (eg, T for tension).
  Draw a free body diagram of the object of interest, based on the labelled picture. If additional objects are involved, draw separate free body diagram for them.

## Slide 36: Hints for problem solving
Choose a convenient coordinate system for each object.
Apply Newton’s second law. The x- and y-components of Newton second law should be taken from the vector equation and written individually. This often results in two equations and two unknowns.
Solve for the desired unknown quantity and substitute the numbers.

## Slide 37: Plenary
What did you learn today?
Important: The pre-session task of session 2 along with the video link of pre-session video, are given at the end of the worksheet.

## Slide 38
PRODUCED BY
FUNDED BY
This programme is funded by the Department for Education
Hugh Baird College, Liverpool has produced this resource on behalf of the Education and Training Foundation
ET-FOUNDATION.CO.UK

## Slide 39: Introduction to engineering mechanics – session 2
Presenter Name
Time and date
Location

## Slide 40: Today’s session outcomes
Recap of session 1
Review answers of pre-session task
Understand types of forces (concurrent, non-concurrent, coplanar, non-contact)
Understand types of loads on simply supported (SS) beams
Understand types of supports used in SS beams
Introduction to next session

## Slide 41: 01
Recap of session 1

## Slide 42: Last week we learnt to:
understand what we will cover in the course
recognise what problem-based learning (PBL) is
understand what the structural features of systems are
construct free body diagrams (FBD)
understand and calculate forces in static systems using Newton’s laws
understand and calculate forces and accelerations using Newton’s laws.

## Slide 43: True or false assessment questions from last session
No resultant force is acting on the planet Mars.
A free-falling accelerating object has a resultant force.
A free-falling object always has a resultant force.
True
False
True
False
True
False
Notes: False
True
False

## Slide 44: Pre-session task – session 2 Pre-session video link: How to Calculate Support Reactions of a Simply Supported Beam with a Point Load - YouTube

## Slide 45: Revisit of PBL scenario from last week EOT Crane | Double Girder | Overhead Crane | EOT Crane Working | How Crane Works? | 3D Animation - YouTube

## Slide 46: Let’s see your answers
Draw the FBD for one girder, using the design details given above.

## Slide 47: Let’s see your answers
b. Calculate the reaction forces at the two ends of the girder.

## Slide 48: Let’s see your answers
c. Evaluate the effect of the trolley movement on the end reactions.
The vertical reaction force size varies with the position of the trolley.

## Slide 49: Let’s see your answers
c. Evaluate the effect of the trolley movement on the end reactions.
When the trolley is moving, there will be forces acting along the girder, such as driving force of the trolley and the friction force against the movement. Hence, to balance these, there should be horizontal opposite reactions at the two ends of the girder. This means, the end supports should restrict both vertical and horizontal movements. The horizontal reaction force at the supports varies along with the magnitude of friction force on trolley, and the direction of the movement of trolley.
Thrust/ Driving force
Friction force
Friction force
Horizontal support reaction
Horizontal support reaction

## Slide 50: True or false assessment questions for pre-session task
The trolley movement exerts vertical friction force on the girder.
The trolley movement exerts both vertical and horizontal reaction forces at end supports of girder.
The driving force is zero when the trolley moves in constant velocity.
True
False
True
False
True
False
Notes: False
True
False

## Slide 51: 02
Experiment – beams, loads and support reactions

## Slide 52: Pre-experiment task
Watch this video and categorise the forces you identified in the double girder AOC system into following categories:
      concurrent forces
      non-concurrent forces
      co-planar forces
      non-contact forces.
System of Forces - YouTube

## Slide 53: Experimental set-up
Required items:
two wooden blocks of generally 5 cm of side length
a wooden/steel beam (you can use a metre ruler)
two bathroom scales or a similar scale
weights – a wooden block, an A4 size book.

## Slide 54: Experimental set-up
Follow the steps listed on the experiment worksheet and complete the results table.
*Note that the reading on the scale is the reaction force exerted by the wooden block on the scale.

## Slide 55: Experiment set-up (4a)
R1
R2
mg
Record the scale readings in the space provided on the experiment worksheet
Mg

## Slide 56: Experiment set-up (4b)
R1
R2
mg
Mg
Record the scale readings in the space provided on the experiment worksheet

## Slide 57: Experiment set-up (4c)
R1
R2
mg
Mg
Record the scale readings in the space provided on the experiment worksheet

## Slide 58: Experiment set-up (4d)
R1
R2
?
?
?
Mg
Record the scale readings in the space provided on the experiment worksheet

## Slide 59: Experiment set-up (4e)
R1
R2
?
?
Mg
Record the scale readings in the space provided on the experiment worksheet

## Slide 60: Experiment set-up (4f)
R1
R2
?
?
Mg
Record the scale readings in the space provided on the experiment worksheet

## Slide 61: Experiment set-up (4g)
R1
R2
?
?
mg
Mg
Record the scale readings in the space provided on the experiment worksheet

## Slide 62: 03
Simply supported (SS) beam analysis

## Slide 63: (698) Strength of Materials: Beams - YouTube
Types of beams
Study the video and give an example of applications for each beam type listed below.
tube beam
box beam
I beam.
Education and Training Foundation

## Slide 64: Types of loads
Point loads
Uniformly distributed loads (UDL)
Non-uniformly distributed loads
Point Load vs. Uniform Distributed Load | Federal Brace
(698) Vector Statics: Distributed Forces - YouTube​
​
Education and Training Foundation

## Slide 65: What is a loading function?
The magnitude of the distributed load of the books is the total weight of the books divided by the length of the shelf
Loading function
Education and Training Foundation

## Slide 66: Types of supports
Types of Support | Support Reactions in a Beam - YouTube
Education and Training Foundation

## Slide 67: True or false assessment questions
The weight of a carpet on the floor is a uniformly distributed load.
The weight of a person is a non-uniformly distributed load.
Roller support reaction has a vertical and a horizonal component.
Education and Training Foundation
True
False
True
False
True
False
Notes: False
True
False

## Slide 68: 04
Summary of the session

## Slide 69: Session 1 and 2 – revisit
In session 1, we learnt …
In session 2, we learnt ...
Education and Training Foundation

## Slide 70: Plenary
What did you learn today?
Education and Training Foundation

## Slide 71: Pre-session tasks for session 3
Task 1: Watch the video in the next slide and list ten applications of beams that you can identify from the video along with a screen-print.
Example answer:
Wind turbine blades
Education and Training Foundation

## Slide 72
Think Lifting is an educational initiative by Lifting Equipment Engineers Association (LEEA).
LEEA has released some videos to support their Schools Engagement Project.
Watch the first video listed on this website.
Think Lifting (leeaint.com)
Pre-session tasks for session 3
Education and Training Foundation

## Slide 73: Next session
In our next session we will be working on:
SS beam analysis
This requires skills and understanding on calculation of moments.
Refer to the link below for self-directed revision on moments:
Moments - Moments, levers and gears - AQA - GCSE Physics (Single Science) Revision - AQA - BBC Bitesize
Education and Training Foundation

## Slide 74
Let’s complete the self-assessment sheet for today’s session
R
A
G
Education and Training Foundation

## Slide 75
PRODUCED BY
FUNDED BY
This programme is funded by the Department for Education
Hugh Baird College, Liverpool has produced this resource on behalf of the Education and Training Foundation
ET-FOUNDATION.CO.UK
Education and Training Foundation

## Slide 76: Introduction to engineering mechanics – Session 3
Presenter Name
Time and date
Location

## Slide 77: Today’s session outcomes
Recap of session 2
Review answers of pre-session task
Calculate the support reactions in SS beams subjected to different loading conditions
Comparison of support reaction of SS beams from experiments and theoretical values
Introduction to next session
Education and Training Foundation

## Slide 78: 01
Recap of session 2

## Slide 79: Last week we learnt to:
understand types of forces (concurrent, non-concurrent, co-planar, non-contact)
understand types of loads on simply supported (SS) beams
understand types of supports used in SS beams
perform an experiment on SS beams and record results.
Education and Training Foundation

## Slide 80: True or false assessment questions
The weight of a carpet on a floor is a uniformly distributed load.
The weight of a person is a non-uniformly distributed load.
Roller support reaction has both vertical and horizonal components.
Education and Training Foundation
True
False
True
False
True
False
Notes: False
True
False

## Slide 81: Pre-session task
Education and Training Foundation

## Slide 82: True or false assessment questions for pre-session task
A wind turbine beam is subjected to only point loads.
Beam analysis is only conducted by civil engineers in the industry.
Each member of a truss shall be considered as a beam.
Education and Training Foundation
True
False
True
False
True
False
Notes: False
False
3. True

## Slide 83: 02
Simply supported (SS) beams analysis

## Slide 84: Beam analysis steps
Construct the FBD of beam
Consider resultant force in vertical (y) direction
Consider resultant force in horizontal (x) direction
Consider the resultant moment around one point (Preferably a point, where a reaction force is acting)
Solve the set of equations to calculate the unknowns (Usually the support reactions)
Education and Training Foundation

## Slide 85: Case 4a – Modelled by teacher
R1
R2
mg
Enter the calculated R1 and R2 values in the space provided on the experiment worksheet
Mg
Beam Calculator Online (Calculate the reactions, Draws Bending Moment, Shear Force, Axial Force) (beamguru.com)
Education and Training Foundation

## Slide 86: Case 4b – It’s your turn
R1
R2
mg
Enter the calculated R1 and R2 values in the space provided on the experiment worksheet
Mg
Education and Training Foundation

## Slide 87: Case 4c – It’s your turn
R1
R2
mg
Enter the calculated R1 and R2 values in the space provided on the experiment worksheet
Mg
Education and Training Foundation

## Slide 88: Case 4d – Modelled by teacher
R1
R2
?
?
?
Enter the calculated R1 and R2 values in the space provided on the experiment worksheet
Mg
Education and Training Foundation

## Slide 89: Case 4e – It’s your turn
R1
R2
?
?
Enter the calculated R1 and R2 values in the space provided on the experiment worksheet
Mg
Education and Training Foundation

## Slide 90: Case 4f – It’s your turn
R1
R2
?
?
Enter the calculated R1 and R2 values in the space provided on the experiment worksheet
Mg
Education and Training Foundation

## Slide 91: Example g – It’s your turn
R1
R2
?
?
Enter the calculated R1 and R2 values in the space provided on the experiment worksheet
mg
Mg
Education and Training Foundation

## Slide 92: True or false assessment questions for experiments worksheet
It is important to consider angular momentum for SS beam analysis.
Support reactions are calculated considering the static equilibrium of the beam.
Resultant force and moments are both considered in the static equilibrium concept.
Education and Training Foundation
True
False
True
False
True
False
Notes: False: The purpose of this question is to highlight the difference between the two terms – moment and momentum
True: The purpose here is to emphasise the static equilibrium term
True: The purpose here is to emphasise the use of both resultant force and moments for equilibrium

## Slide 93: 03
Summary of the session

## Slide 94: Plenary
In session 3, we learnt...
In session 2, we learnt...
What did you learn today?​
Education and Training Foundation

## Slide 95: Suppose now we have designed the end supports to provide the required reactions.
What are the possible health and safety risks associated with poorly designed beams?
Education and Training Foundation
Is that all that is required?
Is the beam/ girder safe to load now?
(698) Bending failure of a softwood beam grain parallel to beam axis: Materials Lab on-line - YouTube
Plenary

## Slide 96: Pre-session tasks for session 4
Task: Watch the two videos below and write the definition and units of:
  shearing stress
  shear force
  bending stress
  bending moment.
(698) Strength of Materials: Analysis of shearing stress - YouTube
(698) Strength of Materials: Bending - YouTube
Education and Training Foundation

## Slide 97
Let’s complete the self-assessment sheet for today’s session
R
A
G
Education and Training Foundation

## Slide 98
PRODUCED BY
FUNDED BY
This programme is funded by the Department for Education
Hugh Baird College, Liverpool has produced this resource on behalf of the Education and Training Foundation
ET-FOUNDATION.CO.UK
Education and Training Foundation

## Slide 99: Introduction to engineering mechanics – session 4
Presenter Name
Time and date
Location

## Slide 100: Today’s session outcomes
Recap of session 3
Conduct case studies on engineering design failures
Calculate shear force of simply supported (SS) beams
Calculate bending moment analysis of SS beams
Model SS beams using beam analysis software/ platforms
Introduction to next session
Education and Training Foundation

## Slide 101: 01
Recap of session 3

## Slide 102: Last week we learnt to:
calculate the support reactions in SS beams subjected to different loading conditions
compare the support reactions of SS beams from experiments with theoretical values.​
Education and Training Foundation

## Slide 103: True or false assessment questions for experiments worksheet
It is important to consider angular momentum for SS beam analysis.
Support reactions are calculated considering the static equilibrium of the beam.
Resultant force and moments are both considered in the static equilibrium concept.
Education and Training Foundation
True
False
True
False
True
False
Notes: False: The purpose of this question is to highlight the difference between the two terms – moment and momentum
True: The purpose here is to emphasise the static equilibrium term
True: The purpose here is to emphasise the use of both resultant force and moments for equilibrium

## Slide 104: Pre-session tasks for session 4
Task: Watch the two videos below and write the definition and units of:
    shearing stress
    shear force
    bending stress
    bending moment.
(698) Strength of Materials: Analysis of shearing stress - YouTube
(698) Strength of Materials: Bending - YouTube
Education and Training Foundation
Notes: Students are expected to have watched these two videos prior to the session.

## Slide 105: What is shear or shearing force?
The shearing force (SF) is defined as the algebraic sum of all the transverse forces acting on either side of the section of a beam or a frame.
Education and Training Foundation

## Slide 106: What is bending moment?
The bending moment (BM) is defined as the algebraic sum of all the forces’ moments acting on either side of the section of a beam or a frame.
Education and Training Foundation

## Slide 107: Sign convention
On the right for shear – up is positive. Notice that both of the following figure show the identical sign convention.
Education and Training Foundation

## Slide 108: True or false assessment questions for pre-session task
Shear force acts perpendicular to the cross section of a body.
Shear stress is maximum at the top of a beam.
Bending stress can be either tensile or compressive.
Education and Training Foundation
True
False
True
False
True
False
Notes: False
False
3. True

## Slide 109: 02
Failure of structures due to shear and bending stress

## Slide 110: Group activity
Get into groups allocated by your teacher. Research one of the following structural failures:
Tacoma Narrows bridge failure
Hyatt Regency walkway collapse
I-35W Mississippi River bridge collapse
Tay Bridge Disaster
Kemper Arena roof collapse
Education and Training Foundation

## Slide 111: Case study guideline
What is the project?
How did the disaster occur?
What are the design failures that caused the disaster?
What is the importance of avoiding such failures?
Answer the questions in a PowerPoint presentation and present it to the class.
Case study duration: 30 mins, Presentation and Q/A time: 10 mins
Education and Training Foundation
Notes: Q/A: question and answer

## Slide 112: 03
Stress analysis of simply supported beams

## Slide 113: Beam analysis steps to calculate shear and bending stress
Construct the FBD of beam
Consider equilibrium in x- and y-directions and write equations to find support reactions.
Draw the FBD of sectioned beam to illustrate shear forces and bending moments
Consider equilibrium of beam sections in x- and y-directions and write equations to find shear force and bending moment.
Education and Training Foundation

## Slide 114: Application to the double girder automatic overhead crane PBL project
When the trolley moves along the girders, each girder is subjected to a point load.
Education and Training Foundation

## Slide 115: Examples from the industry
(7) Bending failure of a softwood beam grain parallel to beam axis: Materials Lab on-line – YouTube
Firefighters and Construction: Beams and Girders: How They Fail (fireengineering.com)
Education and Training Foundation

## Slide 116: Case 4a – Modelled by teacher
R1
R2
mg
This is the same as example 4a that we did in session 2 and 3 to calculate R1 and R2.
Use the same beam dimensions and mass values from previous session worksheets.
Mg
Education and Training Foundation

## Slide 117: Case 4a – Modelled by teacher
R1
R2
mg
Mg
x
Education and Training Foundation

## Slide 118: Shear force and bending moment diagrams for case 4a
Beam Calculator Online (Calculate the reactions, Draws Bending Moment, Shear Force, Axial Force) (beamguru.com)
Education and Training Foundation

## Slide 119: Why do we calculate shear force and bending moment? How are these quantities used for design of SS beams?
(24) ANSYS Workbench Tutorial - Simply Supported Beam - Center Load - PART 2 - YouTube
Education and Training Foundation

## Slide 120: Case 4b – It’s your turn – Draw the shear force and bending moment diagram
R1
R2
mg
Mg
This is the same as example 4b that we did in session 2 and 3 to calculate R1 and R2.
Use the same beam dimensions and mass values from previous session worksheets.
Education and Training Foundation

## Slide 121: Case 4c – It’s your turn – Draw the shear force and bending moment diagram
R1
R2
mg
Mg
This is the same example as 4c that we did in session 2 and 3 to calculate R1 and R2.
Use the same beam dimensions and mass values from previous session worksheets.
Education and Training Foundation

## Slide 122: Case 4d – It’s your turn – Draw the shear force and bending moment diagram
R1
R2
?
?
?
Mg
This is the same as example 4d that we did in session 2 and 3 to calculate R1 and R2.
Use the same beam dimensions and mass values from previous session worksheets.
Beam Calculator Online (Calculate the reactions, Draws Bending Moment, Shear Force, Axial Force) (beamguru.com)
Education and Training Foundation

## Slide 123: Case 4e – It’s your turn – Draw the shear force and bending moment diagram
R1
R2
?
?
Mg
This is the same as example 4e that we did in session 2 and 3 to calculate R1 and R2.
Use the same beam dimensions and mass values from previous session worksheets.
Education and Training Foundation

## Slide 124: Case 4f – It’s your turn – Draw the shear force and bending moment diagram
R1
R2
?
?
Mg
This is the same as example 4f that we did in session 2 and 3 to calculate R1 and R2.
Use the same beam dimensions and mass values from previous session worksheets.
Education and Training Foundation

## Slide 125: Example 4g – It’s your turn – Draw the shear force and bending moment diagram
R1
R2
?
?
mg
Mg
This is the same as example 4g that we did in session 2 and 3 to calculate R1 and R2.
Use the same beam dimensions and mass values from previous session worksheets.
Education and Training Foundation

## Slide 126: Three assessment questions for shear force and bending moment calculations
Match the loading arrangements with suitable shear force and bending moment diagrams.
Loading arrangement | Shear force diagram | Bending moment diagram
Education and Training Foundation
Notes: 1st row – Uniformly distributed
2nd row: Point load
3rd row: Linearly distributed

## Slide 127: 04
Summary of the session

## Slide 128: Plenary
In session 3, we learnt...
In session 4, we learnt...
What did you
learn today?​
Design failures
Education and Training Foundation

## Slide 129: Pre-session tasks for session 5
Task: Watch the video given and explain the conservation of momentum principle along with the equations. Then answer the following question using this knowledge on momentum.
An engineer, holding a steel wrench in his hand, was working outside of the International Space Station (ISS). He was attached to the ISS by a wire rope. Due to some mechanical issue, the rope is disconnected from the ISS resulting in the engineer floating motionless in space. How can the engineer get back to the ISS?
(7) Applications of Law of Conservation of Momentum (GA_M-NLM22) – YouTube
Education and Training Foundation

## Slide 130
Let’s complete the self-assessment sheet for today’s session
R
A
G
Education and Training Foundation

## Slide 131
PRODUCED BY
FUNDED BY
This programme is funded by the Department for Education
Hugh Baird College, Liverpool has produced this resource on behalf of the Education and Training Foundation
ET-FOUNDATION.CO.UK
Education and Training Foundation

## Slide 132: Introduction to engineering mechanics – session 5
Presenter Name
Time and date
Location

## Slide 133: Today’s session outcomes
Recap of session 4
Review answers of pre-session task
Calculate momentum of moving objects
Understand principle of conservation of momentum
Calculate velocity or mass using conservation of momentum
Introduce the next session
Education and Training Foundation

## Slide 134: 01
Recap of session 4

## Slide 135: Last week we learnt to:
conduct case studies on engineering design failures
calculate shear force of simply supported (SS) beams
calculate bending moment analysis of SS beams
model SS beams using beam analysis software/platforms.
Education and Training Foundation

## Slide 136: Three assessment questions for shear force and bending moment calculations
Match the loading arrangements with suitable shear force and bending moment diagrams.
Loading arrangement | Shear force diagram | Bending moment diagram
Education and Training Foundation
Notes: 1st row – Uniformly distributed
2nd row: Point load
3rd row: Linearly distributed

## Slide 137: Pre-session tasks for session 5
Task: Watch the video given and summarise the conservation of momentum principle along with the equations. Then answer the following question using the knowledge on momentum.
An engineer, holding a steel wrench in his hand, was working outside of the International Space Station (ISS). He was attached to the ISS by a wire rope. Due to some mechanical issue, the rope disconnected from the ISS resulting in the engineer floating motionless in space. How can the engineer get back to the ISS?
(7) Applications of Law of Conservation of Momentum (GA_M-NLM22) – YouTube
Education and Training Foundation

## Slide 138: Answer to the pre-session task
(24) Rocket Propulsion - Due to Conservation of Momentum | Physics with Professor Matt Anderson | M9-03 - YouTube
Education and Training Foundation

## Slide 139: Application of momentum knowledge to the design of double girder automatic overhead crane PBL project
Modelling the movement of the trolley along the girder
Other examples:
Jet and rocket engines, the jet pump, the Pelton turbine.
Flow through a sudden enlargement, a convergent nozzle, a pipe bend and a pipe junction.
Education and Training Foundation

## Slide 140: 02
Linear momentum experiment

## Slide 141: What is momentum?
Newton, in describing moving objects, talked about their “quantity of motion”, a value based both on the inertia or mass (m) of the object and its velocity (v)
“Quantity of motion” is momentum (p)
Momentum Conservation Principle (physicsclassroom.com)
What is the unit?
Education and Training Foundation
Notes: Unit: kg.ms^(-1)

## Slide 142: Impulse
The impulse of a force is defined as the product of the average force (F) and the time (t) interval for which the force acts on the body.
Impulse - Collisions, explosions and impulse - Higher Physics Revision - BBC Bitesize
Impulse
Change in momentum
What is the unit?
Education and Training Foundation
Notes: Unit: Ns

## Slide 143: Conservation of momentum
The conservation of momentum states that when a system of interacting objects is not influenced by outside forces (like friction), the total momentum of the system cannot change.
Education and Training Foundation
,
, so
Conservation of Momentum (nasa.gov)

## Slide 144: Elastic or inelastic?
An elastic collision loses no energy. The deformation on collision is fully restored.
In an inelastic collision, energy is lost and the deformation may be permanent.
Education and Training Foundation

## Slide 145: Verification of the principle of conservation of momentum
Physics Simulation: Collisions (physicsclassroom.com)
Follow the instructions given on the experiment handout and complete the results table.
Education and Training Foundation

## Slide 146: True or false assessment questions for experiments worksheet
When two objects collide inelastically the momentum can be conserved.
An elastic collision is a collision in which there is no net loss in kinetic energy in the system as a result of the collision.
A head-on collision means momentum is conserved but kinetic energy is not.
Education and Training Foundation
True
False
True
False
True
False
Notes: True
True
False

## Slide 147: 03
Momentum calculations

## Slide 148: Problem 1
Foundation piles for tall buildings are hammered into the ground using a pile-driver. This is similar to the one shown in the link below that lifts 1000 kg hammer to a distance above the top of a pile, and then allows it to drop.
Movax Pile Driving Equipment | Piling Hammers for sale from Premier Rock Machinery - IndustrySearch Australia
The impulse 61.7 kN.s is delivered by this pile-driver in
What is the force exerted by the hammer on the pile?
Education and Training Foundation
Notes: Answer: 29.4 x 10^6 N = 29.4 MN

## Slide 149: Problem 2
A satellite with a mass of 12,000 kg and a speed of 600 m/s fires a thruster exerting a force of 600 kN at a 30° angle with the current path as shown below. The thruster is turned off after completing a 90 degree turn as shown below.
How long was the thruster on?
What is the final velocity?
F
30°
600 m/s
Education and Training Foundation

## Slide 150: Problem 2 – answer
Education and Training Foundation

## Slide 151: Problem 3
Two carts, each with a spring bumper, collide head-on. At one point during the collision, both carts are at rest for an instant. At that instant, the kinetic energy that the carts originally possessed is almost completely:
lost to friction
transformed into heat and sound
converted into kinetic energy in the spring bumpers
converted into potential energy in the spring bumpers.
Education and Training Foundation
Notes: Answer: D

## Slide 152: True or false assessment questions for the session 5
Correct units for momentum is J.s.
In an inelastic collision, the energy that appears to be missing is converted into heat and force.
Momentum is a vector.
Education and Training Foundation
True
False
True
False
True
False
Notes: False
False
True

## Slide 153: 04
Summary of the session

## Slide 154: Plenary
What did you learn today?​
Education and Training Foundation

## Slide 155: Pre-session task for session 6
V
(42) Workplace safety - Overhead cranes and hazard zones - YouTube
Discuss the three risks involved with overhead cranes operation and safety precautions used in the industry.
Example risk: side pulling of load
Education and Training Foundation

## Slide 156
Let’s complete the self-assessment sheet for today’s session
R
A
G
Education and Training Foundation

## Slide 157
PRODUCED BY
FUNDED BY
This programme is funded by the Department for Education
Hugh Baird College, Liverpool has produced this resource on behalf of the Education and Training Foundation
ET-FOUNDATION.CO.UK
Education and Training Foundation

## Slide 158: Introduction to engineering mechanics – session 6
Presenter Name
Time and date
Location

## Slide 159: Today’s session outcomes
Recap of session 5 and review answers of pre-session task
Understand the terms and application of tractive force and braking force
Understand different types of mechanical energy
Calculate mechanical energy for given systems
Calculate power in mechanical systems
Introduction to next session
Education and Training Foundation

## Slide 160: 01
Recap of session 5

## Slide 161: Last week we learnt to:
calculate momentum of moving objects
calculate impulse applied on a system
calculate velocity or mass using conservation of momentum
discuss safety issues related to the moving trolley of double girder automated overhead crane (AOC).
Education and Training Foundation

## Slide 162: True or false assessment questions from session 5
Correct units for momentum is J.s.
In an inelastic collision, the energy that appears to be missing is converted into heat and force.
Momentum is a vector.
Education and Training Foundation
True
False
True
False
True
False
Notes: False
False
True

## Slide 163: Pre-session task for session 6
V
(42) Workplace safety - Overhead cranes and hazard zones - YouTube
Discuss the three risks involved with overhead cranes operation and safety precautions used in the industry.
Example risk: side pulling of load
Education and Training Foundation

## Slide 164: Risks
side pulling of weight attached
collision of trolleys
?
?
side pull detection sensors
anti-collision sensors
?
?
Safety precautions
Education and Training Foundation

## Slide 165: 02
Force and motion

## Slide 166: Equations of motion
t = time
u = velocity at t = 0
v = velocity at t = t
a = acceleration in t duration
s = displacement in t duration
Education and Training Foundation

## Slide 167: Knowledge assessment
https://www.bbc.co.uk/bitesize/guides/zxd9w6f/revision/7
v
Education and Training Foundation

## Slide 168: What is tractive force?
Tractive force is the force needed to overcome the resistance caused by friction when two bodies slide or roll on each other.
The tractive force between a car wheel and the surface can be expressed as
F = μt W
= μt m ag
Where:
F = traction effort or force acting on the wheel from the surface (N)
μt = traction – or friction – coefficient between the wheel and the surface W = weight or vertical force between wheel and surface (N)
m = mass on the wheel (kg)
ag = acceleration of gravity (9.81 m/s2)
Car - Traction Force (engineeringtoolbox.com)
Education and Training Foundation

## Slide 169: What is braking force?
Alternatively known as brake power, the braking force refers to the total amount of force exerted on a moving body that causes it to slow to a halt.
The body or the vehicle must be traveling at a known constant velocity for this force to be calculated correctly. The brake force is measured in newtons “N.”
Kinetic energy when braking started = Braking Force × Distance
Braking Force Calculator - Calculator Academy
Education and Training Foundation

## Slide 170: Group activity on stopping distance
Physics Simulation: Stopping Distance (physicsclassroom.com)
StoppingDistance (physicsclassroom.com)
Stopping Distance Concept Checker (physicsclassroom.com)
This simulation provides a good understanding on the work-energy relationship.
The activity sheet can be accessed here.
Quiz on the work-energy concept can be accessed here.
Education and Training Foundation

## Slide 171: 03
Energy and power

## Slide 172: Kinetic energy
The kinetic energy for a mass in motion is
  K.E. = ½mv2
  m is mass (kg)
  v is speed or velocity (m/s)
  K.E is kinetic energy (J)
Kinetic energy - Motion and energy transfer - GCSE Physics (Single Science) Revision - OCR 21st Century - BBC Bitesize
v
Education and Training Foundation

## Slide 173: Gravitational potential energy
If an object is raised, its store of gravitational potential energy increases. As it falls, its gravitational potential energy decreases. The amount of gravitational potential energy stored by an object at height can be calculated using the equation:
Where:
gravitational potential energy (G.P.E.) is measured in joules (J)
mass (m) is measured in kilograms (kg)
gravitational field strength (g) is measured in newtons per kilogram (N/kg)
height (h) is measured in metres (m).
Education and Training Foundation

## Slide 174: Elastic potential energy (E.P.E.)
This potential energy defines how much work the spring can do on an object
Where:
E.P.E. is measured in joules (J)
The spring constant, k, is measured in (N/m)
The extension, x, is measured in metres (m)
Energy stored in a spring - Forces and elasticity - AQA - GCSE Physics (Single Science) Revision - AQA - BBC Bitesize
Education and Training Foundation

## Slide 175: Knowledge assessment
Changes in energy stores test questions - AQA - GCSE Physics (Single Science) Revision - BBC Bitesize
Education and Training Foundation

## Slide 176: Mechanical energy
Mechanical energy is the ability of an object to do work. It is the sum of the potential energy of an object (gravitational or elastic) and its kinetic energy.
Mechanical Energy =
Mechanical Energy: What Is It and How Does It Work? (justenergy.com)
Education and Training Foundation

## Slide 177: Work done
Work is the amount of energy transferred to an object by an external force when it is moved over a certain distance by that force.
Where:
work, W, is measured in joules (J)
force, F, is measured in newtons (N)
displacement, s, is measured in metres (m).
Education and Training Foundation

## Slide 178: Power
The rate at which this energy is transferred is called power.
The equation used to calculate the power is:
Where:
power, P, is measured in watts (W)
work done, E, is measured in joules (J)
time, t, is measured in seconds (s).
Power - Power and efficiency - Edexcel - GCSE Physics (Single Science) Revision - Edexcel - BBC Bitesize
Education and Training Foundation

## Slide 179: Knowledge assessment
Work, power and efficiency test questions - AQA Trilogy - GCSE Combined Science Revision - BBC Bitesize
Education and Training Foundation

## Slide 180: 04
Industrial applications

## Slide 181: Scenario 1
‪Pendulum Lab‬ (colorado.edu)
Select the energy tab in Pendulum Lab
Study how the kinetic energy and the potential energy varies with the pendulum movement.
Education and Training Foundation

## Slide 182: Problem 1
The trolley is moving at a constant speed of 0.7 m/s. Due to a power failure, the trolley instantly stops moving and the mass attached to the trolley pulls to one side.
Calculate the raised height of the mass attached to the trolley.
Mass of the trolley: 25 kg
Mass attached to the trolley: 250 kg
Education and Training Foundation
V

## Slide 183: Problem 1 – Answer
‪
Mass of the trolley: 25 kg
Mass attached to the trolley: 250 kg
Speed: 0.7 m/s
Mechanical energy of initial system = Mechanical energy of final system
Education and Training Foundation

## Slide 184: Calculate the horizontal displacement of the mass attached to the trolley, if the length of the cable is 3 m.
3 m
(3 – h) m
h
Education and Training Foundation

## Slide 185: Scenario 2
‪Masses and Springs‬ (colorado.edu)
Select the energy tab in Masses and Springs Lab
Study how the kinetic energy and the potential energy varies with the spring length variation
Education and Training Foundation

## Slide 186: Problem 2
Two carts, each with a spring bumper, collide head-on. At one point during the collision, both carts are at rest for an instant. At that instant, the kinetic energy that the carts originally possessed is almost completely:
lost to friction
transformed into heat and sound
converted into kinetic energy in the spring bumpers
converted into potential energy in the spring bumpers.
Education and Training Foundation
Notes: Answer: D (this is a question from session 5)

## Slide 187: 05
Summary of the session

## Slide 188: Plenary
What did you learn today?​
v
Education and Training Foundation

## Slide 189: Pre-session tasks for session 7
Task:
Watch the two videos given below and:
Explain different energy generation methods used in the world.
Discuss four renewable energy generation methods in the UK?
(42) A guide to the energy of the Earth - Joshua M. Sneideman – YouTube
(42) Renewable Energy 101 | National Geographic - YouTube
Education and Training Foundation

## Slide 190
Let’s complete the self-assessment sheet for today’s session
R
A
G
Education and Training Foundation

## Slide 191
PRODUCED BY
FUNDED BY
This programme is funded by the Department for Education
Hugh Baird College, Liverpool has produced this resource on behalf of the Education and Training Foundation
ET-FOUNDATION.CO.UK
Education and Training Foundation

## Slide 192: Introduction to engineering mechanics – session 7
Presenter Name
Time and date
Location

## Slide 193: Today’s session outcomes
Recap of session 6 and review answers of pre-session task
Understand rotational kinetic energy and moment of inertia
Identify types of power sources and practical applications (flywheels, springs, height, pressurised fluids)
Understand the need for renewable energy sources and sustainable materials used to reduce energy requirement
Education and Training Foundation

## Slide 194: 01
Recap of session 6

## Slide 195: Last week we learnt to:
understand the terms and application of tractive force and braking force
understand different types of mechanical energy
calculate mechanical energy for given systems
calculate power in mechanical systems.
Education and Training Foundation

## Slide 196: Knowledge check
A trolley filled with construction materials of mass 1500 kg, travelling at a steady speed on a material transport line, has a kinetic energy of 200 kJ. What is the speed of the trolley?
      0.52 m/s
      16.3 m/s
      266.7 m/s
Education and Training Foundation
Notes: 16.3 m/s

## Slide 197: Pre-session tasks for session 6
Task: Watch the two videos given below and
Explain different energy generation methods used in the world.
Discuss four renewable energy generation methods in your country?
(42) A guide to the energy of the Earth - Joshua M. Sneideman – YouTube
(42) Renewable Energy 101 | National Geographic - YouTube
Education and Training Foundation

## Slide 198: Answer to the pre-session task
Education and Training Foundation

## Slide 199: In class task – continuation of the pre-session task
Identify the different energy conversions involved in the four renewable energy generation methods.
Example: Hydropower
Potential energy of stored water by the dam
Kinetic energy of flowing water as it moves downstream
Turbines and generators to convert that kinetic energy into electricity
Education and Training Foundation

## Slide 200: 02
Rotational kinetic energy and moment of inertia

## Slide 201: Moment of inertia
Pre-video question:
A solid disc and a ring that have same mass are rotated.
Which statement is correct?
  Both possess the same difficulty to rotate.
  The ring is more difficult to rotate than the disc.
  The disc is more difficult to rotate than the ring.
https://www.youtube.com/watch?v=lNx0yPdl960
Education and Training Foundation

## Slide 202: Rotational kinetic energy
What are the rotational objects used to store energy?
https://www.youtube.com/watch?v=CHQOctEvtTY
https://www.youtube.com/watch?v=W9fPGXyvrVM
Education and Training Foundation

## Slide 203: Flywheel
Where have you seen flywheels being used?
https://www.youtube.com/watch?v=EMazLuxpzxE
Education and Training Foundation

## Slide 204: Energy storing methods
What are the methods to store energy?
Can we store electricity before distribution to houses?
How is the electricity distributed?
Education and Training Foundation

## Slide 205: 03
Overall course knowledge assessment

## Slide 206: Overall knowledge – practice question
In the session 1, worksheet 1, question 2, we completed a task that required you to calculate the force required to move the traversing trolley at a constant velocity along the girder.
This can be used to calculate the amount of work done by the trolley per second, which is part of the design information required by engineers to select a suitable motor to provide the required force.
Education and Training Foundation

## Slide 207: Overall knowledge – practice question cont.
Figure: Double girder AOC system with the traversing trolley
Education and Training Foundation

## Slide 208: Overall knowledge – practice question cont.
Part 1
As part of the design process, the engineers have decided to analyse the cable tension for different configurations of the hoist cable attached to the traversing trolley.
Case: Double cable hoist as given below with 1 tonne attached to the hook.
Calculate the tension of the ropes.
5 kg
Education and Training Foundation

## Slide 209: Answer: tension of the ropes.
Education and Training Foundation

## Slide 210: Overall knowledge – practice question cont.
Part 2
Design details:
The trolley has a mass of 15 kg. The kinetic friction coefficient between the girder and the trolley has been calculated as 0.73.
Education and Training Foundation

## Slide 211: Overall knowledge – practice question cont.
Draw the free body diagram (FBD) of the stationary trolley.
Calculate the reaction forces acting on the stationary trolley.
Calculate the frictional force acting on the trolley when the trolley is moving.
Calculate the force required to move the traversing trolley in constant velocity along the girder.
If the operating velocity is 0.7 m/s, calculate the work done by the trolley per second.
Education and Training Foundation

## Slide 212: Answer: overall knowledge – practice question
Education and Training Foundation

## Slide 213: Answer: overall knowledge – practice question
Education and Training Foundation

## Slide 214: Answer: overall knowledge – practice question
Education and Training Foundation

## Slide 215: Answer: overall knowledge – practice question
Education and Training Foundation

## Slide 216: Answer: overall knowledge – practice question e) Work done by the trolley per second.
Force to move the trolley at constant velocity = 7.3 kN
Operating velocity = 0.7 m/s
Work done = J
Work done per second = J/s
= W
Hence, work done by the trolley per second = W
= W
= kW
Education and Training Foundation

## Slide 217: In-class exam – duration: One hour
Topic: Application of Newton’s laws
Assessment objectives:
    Construct free body diagrams (FBD).
    Calculate forces in static systems using Newton’s first and third law.
    Calculate forces and accelerations using Newton’s second law.
    Calculate momentum of moving objects.
    Calculate impulse using principle of momentum.
    Calculate mechanical energy for given systems.
    Calculate quantities using conservation energy principle.
    Calculate power in mechanical systems.
Education and Training Foundation

## Slide 218: 04
Renewable energy – further readings

## Slide 219: Further readings
Use of renewable energy and sustainable future
https://www.nhm.ac.uk/discover/renewable-energy.html
Sustainable materials and design approaches to reduce energy requirement in houses
https://ww3.rics.org/uk/en/modus/natural-environment/renewables/the-future-of-sustainable-building-materials.html
https://eandt.theiet.org/content/articles/2021/10/the-green-house-effect-building-greener-to-tackle-climate-change/
Education and Training Foundation

## Slide 220: 05
Summary of the session

## Slide 221: Plenary
What did you learn today?​
Education and Training Foundation

## Slide 222
Let’s complete the self-assessment sheet for today’s session
R
A
G
Education and Training Foundation

## Slide 223
PRODUCED BY
FUNDED BY
This programme is funded by the Department for Education
Hugh Baird College, Liverpool has produced this resource on behalf of the Education and Training Foundation
ET-FOUNDATION.CO.UK
Education and Training Foundation